## Slide 1: CPEN 411: Computer Architecture Slide Set #10: Introduction to Parallel Processing
Tor Aamodt
aamodt@ece.ubc.ca

## Slide 2: Introduction to Slide Set 10
So far in the course we have learned how an individual processor core works. In this slide set start thinking about what happens if we connect multiple cores together.
Here we focus only on introducing the benefits and challenges of having multiple cores.
Next week: Programming GPUs with NVIDIA CUDA

## Slide 3: Learning Objectives
By the time we finish talking about this slide set in lectures you should be able to:
  Explain the challenges of obtaining performance using parallel processing.

## Slide 4: Why (Explicitly) Parallel Computing?
3X
Concern about end of Moore’s Law… Lots of interest in Multiprocessors.

## Slide 5: Challenges of Parallel Processing
First challenge is % of program inherently sequential
Suppose we want to obtain an 80X speedup from 100 processors (versus 1 processor). What fraction of original program can be sequential?
  10%
  5%
  1%
  <1%

## Slide 6: Amdahl’s Law Answers

## Slide 7: Challenges of Parallel Processing
Second challenge is long latency to remote memory
Suppose 32 CPU MP, 2GHz, 200 ns remote memory, all local accesses hit memory hierarchy and base CPI is 0.5. (Remote access = 200/0.5 = 400 clock cycles.)
What is performance impact if 0.2% instructions involve remote access?
  1.5X
  2.0X
  2.5X

## Slide 8: Solution
CPI = Base CPI + (Remote request rate x Remote request cost)
CPI = 0.5 + 0.2% x 400 = 0.5 + 0.8 = 1.3
If no communication, 1.3/0.5 or 2.6 faster than 0.2% instructions involve remote access

## Slide 9: Flynn’s Taxonomy
Flynn classified by data and control streams in 1966
Single Instruction Single Data (SISD) A machine supporting a single thread of execution. | Single Instruction Multiple Data SIMD A computer in which each instruction operates on multiple data elements at once (e.g., think of vectors and matricies)
Multiple Instruction Single Data (MISD) (this combination doesn’t make sense) | Multiple Instruction Multiple Data MIMD A computer in which there are multiple independent threads each operating on their own data.
ALU
I
D
ALU
I
D
ALU
ALU
ALU
D
D
D
ALU
I
D
ALU
I
D
ALU
I
D
Notes: Reminder, you do need to know the definition in text, the image are just for illustration

## Slide 10: SIMD: Operation on Vectors
SIMD architectures operate on “vectors” of data.
Consider the calculation Z = X + Y, where X, Y and Z are vectors:
  X = (x0, x1, … xn-1) and Y = (y0, y1, … yn-1)
  Z = (x0 + y0 , x1 + y1 , … , xn-1 + yn-1 )
SIMD uses vector registers each holding multiple numbers.
Operate on entire vector register at once.

## Slide 11
Example: Z = X + Y
+
+
+
+
+
+
ADDV.D V3, V1, V2
V3
V2
V1
MIPS64
DADDIU R4, Rx, 48 ; last address to load
Loop: L.D F0, 0(Rx) ; load X(i)
L.D F1, 0(Ry) ; load Y(i)
ADD.D F2, F1, F0 ; X(i) + Y(i)
S.D F2, 0(Rz) ; store into Z(i)
ADDIU Rx,Rx,#8 ; increment index to X
ADDIU Ry,Ry,#8 ; increment index to Y
ADDIU Rz,Rz,#8 ; increment index to Z
DSUB R20, R4, Rx ; compute bound
BNEZ R20, Loop ; check if done
VMIPS
LV V1,Rx
LV V2,Ry
ADDV.D V3,V1,V2
SV V3,Rz

## Slide 12: Multicore Processors
P
1
$
Inter
connection network
$
P
n
Memory (DRAM)
Each Pi is a processor like those studied earlier in the course. The boxes labeled “$” are caches.
Multiple processor cores on a single chip.
Processors are connected via an interconnection network (bus, crossbar, ring, mesh).
Cache

## Slide 13: How to program?
Easiest: Multiprogramming
  Separate single thread applications
  Used today for “Cloud Computing”
For some programs: Parallelizing Compiler
  Input C/C++/Fortran; Output parallel program
General: Parallel APIs / Languages
  APIs: Pthreads, OpenMP, MPI
  Languages: CUDA, OpenCL, High Performance Fortran, Erlang, Sisal

## Slide 14: POSIX threads (pthreads)
#define N (1024*1024)
double data[N], sum[2];
void *foo() { int i; for(i=0;i<N/2;i++) sum[0] += data[i]; }
void *bar() { int i; for(i=0;i<N/2;i++) sum[1] += data[i+N/2]; }
int main(int argc, char *argv[])
{
pthread_t f, b;
// load data with values here...
pthread_create(&f, NULL, foo, NULL);
pthread_create(&b, NULL, bar, NULL);
pthread_join(f, NULL);
pthread_join(b, NULL);
double total = sum[0]+sum[1];
// do something with total here
return 0;
}
Create two new threads. Operating system can schedule them on different cores so they run at same time (concurrently).
creates a new thread
that starts running
code in foo().
main()
foo()
bar()

## Slide 15
P
1
$
Inter
connection network
$
P
n
Memory (DRAM)
Cache
thread 1: foo()
thread 1: bar()
thread 0: main()

## Slide 16: One thread per core?
Multiple cores enable multiple threads to run at the same time if we have one thread on each core.
However, with one thread per core, cache misses can cause each core to be idle most of the time.
Would like to “multiplex” more than one thread per core, but an operating system context switch takes far longer than the latency of a cache miss.

## Slide 17: Hardware Idle Due to Memory Latency

## Slide 18: Hardware Multithreading?
If operating system is too slow to context switch, can we have hardware do this for us?
Answer: Yes, but there is some area and complexity overhead.

## Slide 19: Fine-Grained Multithreading

## Slide 20: Parallel Communication Models
Communication occurs by explicitly passing messages among the processors: message-passing
  Benefit: Scalable -- systems with 100K processors use this
  Drawback: Programmer effort to divide up data among processors and explicitly communicate changes to data.
Communication occurs through a shared address space via load and store instructions: shared memory
  Benefit: Less initial work for programmer
  Drawback: Not as scalable. Effort to obtain high performance

## Slide 21: Shared Memory
We focus on shared memory as this is what you see in today’s microprocessors (e.g., Intel Core i5, i7; and mobile system-on-chips such as Snapdragon).
Communication occurs via memory—from earlier example:
foo() writes sum[0]
bar() writes sum[1]
main() reads sum[0] and sum[1] and adds them.

## Slide 22: Two Shared Memory Concepts
Memory Consistency Model
  Specifies ordering of updates to different locations that are allowed by hardware
Cache Coherence Protocol
  Ensures updates to any single location by one thread become visible to threads on other cores

## Slide 23: Intuitive “Memory Model”
P
Disk
Memory
L2
L1
100:34
100:35
100:67
Reading an address should return the “last value written to that address”

## Slide 24: Another Silly Analogy
Instructor tells ECE office to change lecture location on SSC (e.g., from MCLD to CHEM), then sends text message to students telling them to check new location on SSC.
Diligent student gets text, immediately checks SSC and sees room is MCLD since ECE office busy and has not yet updated SSC.
Diligent student goes to wrong room!
Instructor sent messages in correct order!
Who is at fault? Solutions?

## Slide 25: Memory Consistency Problem
Example:
P1: A = 0; P2: B = 0;
... ...
A = 1; B = 1;
L1: if (B == 0) ... L2: if (A == 0) ...
Possible for both “if” statements L1 & L2 to be true?
What if load is executed before store due to out of order execution?
Memory consistency model specifies rules for ordering of loads and stores accessing different locations and executed in different threads

## Slide 26: Caches Critical for Performance
Reduce average latency
Reduce average bandwidth
Data is logically transferred from producer to consumer via memory
  store reg --> mem
  load reg <-- mem
P
P
P
Problem: What happens when store & load are executed on different processors?
Many processors can share data efficiently

## Slide 27: Cache Coherence Problem
  Processors see different values for u after event 3
  With write back caches, value written back to memory depends on order of which cache writes back value first
  Unacceptable situation for programmers
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7

## Slide 28: Cache Coherence Example
Must invalidate before step 3
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7
u = 7

## Slide 29: Single Core Performance
P
T
i
m
e
(
s
)
1
0
0
7
5
5
0
2
5
Performance depends heavily on memory hierarchy
Managed by hardware
Time spent by a program
  Timeprog = Busy + Data Access
Data access time can be reduced by:
  Optimizing machine
    bigger caches, lower latency...
  Optimizing program
    temporal and spatial locality
B
u
s
y
-
u
s
e
f
u
l
D
a
t
a
-
l
o
c
a
l

## Slide 30: Multicore Performance
P
0
P
1
P
2
P
3
B
u
s
y
-
o
v
e
r
h
e
a
d
B
u
s
y
-
u
s
e
f
u
l
D
a
t
a
-
l
o
c
a
l
S
y
n
c
h
r
o
n
i
z
a
t
i
o
n
D
a
t
a
-
r
e
m
o
t
e
T
i
m
e
(
s
)
T
i
m
e
(
s
)
1
0
0
7
5
5
0
2
5
1
0
0
7
5
5
0
2
5
(
a
)
S
e
q
u
e
n
t
i
a
l
e
s
s
o
r
s
(
b
)
P
a
r
a
l
l
e
l
w
i
t
h
f
o
u
r
p
r
o
c