## Slide 1: CPEN 411: Computer Architecture Slide Set #13: Tomasulo’s Algorithm (Textbook: 2.1, 2.4, 2.5)
Instructor: Dr. Tor M. Aamodt
aamodt@ece.ubc.ca
Background: Pentium Pro die photo (first x86 with out of order execution)

## Slide 3: Introduction to Slide Set 13
Once we enable out-of-order execution we have to consider both WAW and WAR hazards. The (out-of-order) scoreboard algorithm handles these hazards by stalling.
Notice that no value is communicated between instructions involved in these WAW or WAR hazards.
In this lecture we will see that it is possible to eliminate the “name dependencies” that require stalling by having the hardware “rename” the locations causing the “name dependencies”.
The specific hardware algorithm we will examine for doing this is called “Tomasulo’s Algorithm”. It is widely used in today’s computers.

## Slide 4: Learning Objectives
After we finish going through these slides you will be able to…
Describe Tomasulo’s algorithm in detail.
Explain the key difference between the Scoreboard algorithm and Tomasulo’s algorithm.
Evaluate instruction timing of MIPS assembly code sequences using Tomasulo’s algorithm.

## Slide 5: Removing Name Dependencies
Name dependencies result from reusing a register:
LD R1, 0(R2)
DADD R3,R1,R3
DADDUI R2,R2,#8 ; reuse R2
LD R1, 0(R2) ; reuse R1
Adding registers to the hardware we have seen previously will reduce name dependencies but only if software is recompiled to use the additional registers.
It is desirable to be able to add registers to hardware and have hardware use them without requiring recompilation.
If we remove the name dependencies, we don’t encounter WAW or WAR hazards at all (but still have RAW hazards).

## Slide 6: Removing Name Dependencies
Basic idea: Introduce new name for each value created
Before:
LD R1, 0(R2)
DADD R3, R1, R3
DADDUI R2, R2,#8
LD R1, 0(R2)
After:
LD T1, 0(R2) ; R1 -> T1
DADD T2, T1, R3 ; R3 -> T2
DADDUI T3, R2, #8 ; R2 -> T3
LD T4, 0(T3) ; R1 -> T4

## Slide 7: Observation and Insight
WAW and WAR can only occur for instructions in the pipeline at the same time.
  So, we don’t really need infinite # of registers!
  One “rename register” per “in flight” instruction
How to implement renaming in hardware?
  Distinguish architecture reg. from rename reg.
  Associate new name (“rename register”, “physical register”, “reservation station ID”, “tag”) with each inflight instruction updating an arch. reg.
  Use table (“rename table”, “register result status”) to map from architecture register → tag (most recent instruction writing this arch. register)
  “Recycle” tag after instruction is complete.

## Slide 8: Tomasulo Algorithm: Historical Context
Developed in mid 1960’s for floating-point unit of IBM 360 model 91
IBM 360 model 91 designed for scientific computing (e.g., NASA)
Notion of instruction set compatibility invented for IBM System/360.
4 FP registers
Anticipated FP unit latencies of 6 cycles for multiply, 18 for divide, 2 for addition; 8 cycles to access memory; no cache.

## Slide 9: Historical Motivation
Design goal for System/360 model 91:
  Sustain CPI as close as possible to 1 on floating-point code
Constraints:
  Binary compatibility had to be maintained. Four registers visible to programmer. Code with many WAW hazards since required fewer instructions in 360/91 ISA.
  Long floating-point function unit latencies
  Separate pipelined floating point adder and multiplier (higher clock frequency)
  Today’s Motivation: Above + cache misses + parallelism between branches < 2.
Design tradeoffs Tomasulo considered
  Adding busy bits to register file (in-order scoreboard)
  Adding “working registers” near function units to improve clock frequency
  Additional function units to eliminate structural hazards
  Impact of software techniques such as “loop unrolling”
However, Tomasulo ended up with a different design…

## Slide 10: Tomasulo Algorithm
Control & buffers distributed with Function Units (FU)
  Buffers called reservation stations; contain pending operands
Register numbers in instructions get replaced by “tags” each of which “points to” a reservation station (RS)
  Effect of this is to “rename” registers
  This “renaming” avoids WAR, WAW hazards which result from reusing the same register name even though no data is passed between the instructions involved.
  Renaming allowed more reservation stations than registers
  Results sent over a “Common Data Bus” which broadcasts results to all Function Units (Fus), and identifies producer “tag” not the consumer
Load and Stores treated as function units with RSs as well
Tomasulo was working on floating-point hardware unit (similar to example in next few slides). Idea extends to integer instructions as well.

## Slide 11: Tomasulo Algorithm
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)‏
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Notes: 11
Resolve RAW memory conflict? (address in memory buffers)‏
Integer unit executes in parallel

## Slide 12: Three Stages of Tomasulo Algorithm
1. Issue—Get instruction from FP Op Queue
  (called “dispatch” in superscalar processors)
  If reservation station free (no structural hazard),
  (a) lookup source operand registers in “register result status” table while
  allocating reservation station.
  (b) update “register result status” table entry of destination register with
  reservation station (this renames destination register)
2. Execute—Operate on operands
  (called “issue” in superscalar processors)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
3. Write result—Finish execution
  Write on Common Data Bus to all units waiting for result; mark reservation station available
Normal data bus = data + destination address (“go to” bus)
Common data bus = data + source tag (“come from” bus)
  64 bits of data + 4 bits of Reservation Station source address (tag)

## Slide 13: Tomasulo Algorithm Components
Reservation Station:
Busy: Indicates whether reservation station is busy
Op: Operation to perform in FU (e.g., “add” or “subtract”)‏
Vj, Vk: Value of Source operands
Qj, Qk: Tags: Identify reservation station producing Vj, Vk
When Qj=0 (no tag), Vj holds valid data
When Qk=0 (no tag), Vk holds valid data
Address: Used to hold effective address for memory (initially set to
immediate offset)‏
Register File (each register has):
Qi—Indicates which reservation station will write register, if such a
reservation station exists. Blank if no pending instructions write register.
Notes: 13
What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)‏
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)‏
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 14: Tomasulo vs. Scoreboard
Tomasulo:
Decentralized Control
Reservation Stations/Renaming
Scoreboard:
Centralized Control
WAR, WAW hazards
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)‏
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Notes: 14
Resolve RAW memory conflict? (address in memory buffers)‏
Integer unit executes in parallel

## Slide 15
Original code:
LD R1, 0(R2)
DADD R3,R1,R3
DADDUI R2,R2,#8
LD R1, 0(R2)
Rewrite using T1, T2, etc… for each new value:
LD T1, 0(R2) ; R1 renamed to T1
DADD T2,T1,R3 ; R3 renamed to T2
DADDUI T3,R2,#8 ; R2 renamed to T3
LD T4, 0(T3) ; R1 renamed to T4

## Slide 16: Tomasulo Algorithm, Renaming Implemented
MUL.D F2,F1,F4
ADD.D F1,F2,F1
FP Registers
Common Data Bus (CDB)‏
FP Op
Queue
Program:
ADD.D F1,F2,F1
MUL.D F2,F1,F4
Cycle 1
F1
F2
F3
F4
FP adders
Add1
Add2
Add3
FP multipliers
Mul1
Mul2
Reservation
Stations
- R[F1]
- R[F2]
- R[F3]
- R[F4]
“Register result status” aka “register alias table” (RAT)
Notes: 16

## Slide 17: Tomasulo Algorithm, Renaming Implemented
MUL.D F2,F1,F4
FP Registers
Common Data Bus (CDB)‏
FP Op
Queue
Program:
ADD.D F1,F2,F1
MUL.D F2,F1,F4
Cycle 2a: ADD.D reads R[F2] & R[F1] values from FP Registers
F1
F2
F3
F4
FP adders
Add1
Add2
Add3
FP multipliers
Mul1
Mul2
Reservation
Stations
ADD.D - R[F2], - R[F1]
- R[F1]
- R[F2]
- R[F3]
- R[F4]
Notes: 17

## Slide 18: Tomasulo Algorithm, Renaming Implemented
MUL.D F2,F1,F4
FP Registers
Common Data Bus (CDB)‏
FP Op
Queue
Program:
ADD.D F1,F2,F1
MUL.D F2,F1,F4
Cycle 2b: F1 “renamed” to “ADD1” (in “register result status”)
F1
F2
F3
F4
ADD1
FP adders
Add1
Add2
Add3
FP multipliers
Mul1
Mul2
Reservation
Stations
ADD.D - R[F2], - R[F1]
-
- R[F2]
- R[F3]
- R[F4]
Notes: 18

## Slide 19: Tomasulo Algorithm, Renaming Implemented
FP adders
Add1
Add2
Add3
FP multipliers
Mul1
Mul2
FP Registers
Reservation
Stations
Common Data Bus (CDB)‏
FP Op
Queue
Program:
ADD.D F1,F2,F3
MUL.D F2,F1,F4
Cycle 3a: MUL.D gets tag “Add1” instead of value “R[F1]”
F1
F2
F3
F4
Add1
ADD.D - R[F2], - R[F3]
MUL.D Add1 - - R[F4]
-
- R[F2]
- R[F3]
- R[F4]
Notes: 19

## Slide 20: Tomasulo Algorithm, Renaming Implemented
FP adders
Add1
Add2
Add3
FP multipliers
Mul1
Mul2
FP Registers
Reservation
Stations
Common Data Bus (CDB)‏
FP Op
Queue
Program:
ADD.D F1,F2,F3
MUL.D F2,F1,F4
Cycle 3b: F2 renamed to “Mul1”
F1
F2
F3
F4
Add1
ADD.D - R[F2], - R[F3]
Mul1
MUL.D Add1 - - R[F4]
-
-
- R[F3]
- R[F4]
Notes: 20

## Slide 21: Tomasulo Algorithm, Renaming Implemented
FP adders
Add1
Add2
Add3
FP multipliers
Mul1
Mul2
FP Registers
Reservation
Stations
Common Data Bus (CDB)‏
FP Op
Queue
Program:
ADD.D F1,F2,F3
MUL.D F2,F1,F4
Cycle 4: result value “X” and name “ADD1” broadcast on CDB
F1
F2
F3
F4
ADD.D - R[F2], - R[F3]
Mul1
MUL.D - X - R[F4]
X
-
- R[F3]
- R[F4]
ADD1, X
Notes: 21

## Slide 22: Assumptions for example
Execution Latency:
  2 clocks for floating point add, subtract;
  10 clocks for floating point multiply
  40 clocks for floating point divide
  Load/Store: 2 cycles
    1st cycle effective address
    2nd cycle access memory
Pipelined function units (start one operation per cycle)
3 floating-point add/subtract reservation stations
2 floating-point multiple reservation stations
Read value into reservation station same cycle as writeback of value to register file (even if the reservation station was “allocated” the same cycle); however, if that means all operands ready, still have to wait until following cycle to “begin execution”

## Slide 23: Tomasulo Example Cycle 1
Clock cycle counter
FU count
down
Instruction stream
3 Load/Buffers
3 FP Adder R.S.
2 FP Mult R.S.

## Slide 24: Tomasulo Example Cycle 2
Note: Hardware allows multiple loads to be overlapped

## Slide 25: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations
MUL.D issued; Load1 completing - what is waiting for it?
Shorthand for
contents of
register F4

## Slide 26: Tomasulo Example Cycle 4
Issue SUB.D; Load2 completing; what is waiting for Load2?
Shorthand for
contents of
memory at
address A1,
where A1 is
effective addr.
of first load
(34+R2)

## Slide 27: Tomasulo Example Cycle 5
Load2 writes to CDB; Timer starts down for Add1, Mult1 (they “begin execution” following cycle -- clock cycle 6)

## Slide 28: Tomasulo Example Cycle 6
Issue ADD.D here despite name dependency on F6?
Yes ADD.D M(A2) Add1
Add2

## Slide 29: Tomasulo Example Cycle 7
Add1 (SUB.D) completing; what is waiting for it?

## Slide 30: Tomasulo Example Cycle 8

## Slide 31: Tomasulo Example Cycle 9

## Slide 32: Tomasulo Example Cycle 10
Add2 (ADD.D) completing; what is waiting for it?

## Slide 33: Tomasulo Example Cycle 11
Write result of ADD.D here?

## Slide 34: Tomasulo Example Cycle 12

## Slide 35: Tomasulo Example Cycle 13

## Slide 36: Tomasulo Example Cycle 14

## Slide 37: Tomasulo Example Cycle 15
Mult1 (MUL.D) completing; what is waiting for it?

## Slide 38: Tomasulo Example Cycle 16
Just waiting for Mult2 (DIVD) to complete

## Slide 39: Faster than light computation (skip a couple of cycles)

## Slide 40: Tomasulo Example Cycle 55

## Slide 41: Tomasulo Example Cycle 56
Mult2 (DIVD) is completing; what is waiting for it?

## Slide 42: Tomasulo Example Cycle 57
Once again: In-order issue, out-of-order execution and out-of-order completion.

## Slide 43: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264, IBM PPC 620 (in CA:AQA 2/e, but not in silicon!)
Many associative comparisons (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc. stores
Non-precise interrupts!
  We will see how to solve this problem later