## Slide 1: CPEN 411: Computer Architecture Slide Set #14: Reorder Buffer, Exceptions, Multiple Instruction Issue
Tor Aamodt
aamodt@ece.ubc.ca
Background: PowerPC 604, one of the first microprocessors with a reorder buffer

## Slide 3: Introduction to Slide Set 14
Out-of-order execution with Tomasulo’s algorithm allows an instruction to execute when its source operands are available. Branch prediction enables us to fetch and decode instructions after a branch before that branch is “resolved”.
To increase performance (reduce CPI) we would like to start executing the instructions fetched and decoded following the predicted branch *before* that branch is resolved. However, we have a problem: out-of-order execution (e.g., using Tomasulo’s algorithm) allows an instruction to update the register file before the branch is “resolved”.
An elegant solution is a hardware structure known as the “re-order buffer”. One reason for calling it an “elegant solution” is it also enables “virtual memory” by supporting an execution model known as “precise exceptions”.

## Slide 4: Learning Objectives
After we finish this set of slides you should be able to:
Explain the motivation for using a reorder buffer and how a reorder buffer operates.
Define multiple instruction issue and explain the motivation for using it.
List two approaches to achieving multiple instruction issue
Evaluate the timing of a processor using multiple issue and Tomasulo’s algorithm.
Evaluate the timing of a processor using multiple issue, Tomasulo’s algorithm and a reorder buffer.
Define what an exception is and list several categories of exceptions.
Explain what is meant by a precise exception.
Explain how the reorder buffer supports precise exceptions.

## Slide 5: Speculative Execution
DIVD R3,R1,R2 ; F:1, D:2, I:3, X:4, W:104
BEQZ R3,Label ; F:2, D:3, I:4, X:105 (“not taken”)
DSUB R4,R4,R3 branch predicted “taken” on cycle 2
Label: DMUL R4,R4,R2 ; F:3, D:4, I:5, X:6, W:?
DADD R4,R4,R1
Goal: Support execution of instructions fetched following a branch prediction before we know if the prediction is correct. Above: Want to execute and broadcast result of DMUL “speculatively” long before branch resolved on cycle 105.
Problem: Such instructions should not update register file because branch might have been predicted incorrectly. Above: cannot let DMUL write to register file until control hazard resolved.

## Slide 6: The Reorder Buffer (ROB)
An elegant solution to this problem is a hardware structure known as a “Reorder Buffer” (ROB).
The reorder buffer is used to divide the “writeback” step into two separate steps: “instruction completion” and “instruction commit”.
An instruction enters “instruction completion” when it finishes execution.
  Instruction broadcasts result on the CDB so dependent instructions can begin execution.
  However, register file not updated yet.
  Instead, the result is “buffered” in the reorder buffer to be written into the register file later.
An instruction enters “instruction commit” when it is the oldest instruction that has completed (and is free from “exceptions”).
  Writes results to register file

## Slide 7: The Reorder Buffer (ROB)
Reorder
Buffer
Inst.
Queue
Adder
Multiplier
Res Stations
Res Stations
Regs
Commit
  Pipeline stages: fetch, decode, issue, execute, complete, commit
Complete
Issue
execute

## Slide 8: The Reorder Buffer (ROB)
The Reorder Buffer (ROB) maintains a “window” of dynamic instructions currently in the pipeline.
The instructions are stored in “first-in first-out” order. That is, the order originally specified by the programmer). Entry allocated in ROB during issue at same time as a reservation station is allocated.
Each ROB entry contains the instruction’s PC, destination register number, destination register value, and an execution status flag.
To make it easier to update the ROB after an instruction executes and to enable easy lookup of results buffered in the ROB but not yet written to the register file we use the ROB entry of the instruction as the tag for renaming instead of reservation station ID.

## Slide 9: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
PC=0x00(DIV R3,R1,R2)
N
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
RAT+Registers
R4
R3
R2
R1
Cycle 3a
DIV issues: allocate ROB
and reservation station
entries, copy R1 and R2
values into reservation
station, and …
branch
Dest
Value
Program Counter
6
0
7
14
multipliers
1 DIVD 14, 7
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 10: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
PC=0x00(DIV R3,R1,R2)
N
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
RAT+Registers
R4
R3
R2
R1
Cycle 3b
... and updates
register alias table (RAT)
since will update R3
if/when DIV commits
branch
Dest
Value
Program Counter
ROB1
6
0
7
14
multipliers
1 DIVD 14, 7
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 11: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 4
BEQZ issued, allocates
ROB and Reservation
Station entries
branch
PC=0x04(BEQZ R3,Label)
N
-
BEQZ ROB1,Loop
PC=0x00(DIV R3,R1,R2)
1 DIVD 14, 7
N
ROB1
6
0
7
14
RAT+Registers
multipliers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 12: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 5a
DMUL issues: allocate ROB
and reservation station
entries, check RAT, copy
register values into
reservation station, and …
branch
PC=0x04(BEQZ R3,Label)
N
-
BEQZ ROB1,Loop
PC=0x00(DIV R3,R1,R2)
1 DIVD 14, 7
N
PC=0x0C(DMUL R4,R4,R2)
N
R4
3 DMUL 6, 7
ROB1
6
0
7
14
RAT+Registers
multipliers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 13: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 5b:
… and updates register
alias table (RAT) since
DMUL should write R4 (if
it commits)
branch
PC=0x04(BEQZ R3,Label)
N
-
BEQZ ROB1,Loop
PC=0x00(DIV R3,R1,R2)
1 DIVD 14, 7
N
PC=0x0C(DMUL R4,R4,R2)
N
R4
3 DMUL 6, 7
ROB1
6
0
7
14
ROB3
RAT+Registers
multipliers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 14: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 6b:
DADD issues, allocates
ROB and Reservation
Station entries, copy R1
value (14) into reservation
station, …
branch
PC=0x04(BEQZ R3,Loop)
N
-
BEQZ ROB1,Loop
PC=0x00(DIV R3,R1,R2)
N
PC=0x0C(DMUL R4,R4,R2)
N
R4
ROB1
6
0
7
14
ROB3
4 DADD ROB3 , 14
PC=0x10(DADD R4,R4,R1)
R4
N
multipliers
1 DIVD 14, 7
3 DMUL 6, 7
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 15: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 6b:
… and updates
RAT entry for R4 since
DADD will write to R4
branch
PC=0x04(BEQZ R3,Loop)
N
-
BEQZ ROB1,Loop
PC=0x00(DIV R3,R1,R2)
N
PC=0x0C(DMUL R4,R4,R2)
N
R4
ROB1
6
0
7
14
ROB4
4 DADD ROB3 , 14
PC=0x10(DADD R4,R4,R1)
R4
N
multipliers
1 DIVD 14, 7
3 DMUL 6, 7
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 16: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 16:
DMUL writes to CDB,
DADD and ROB get
value, but register file
not updated
branch
PC=0x04(BEQZ R3,Loop)
N
-
BEQZ ROB1,Loop
PC=0x00(DIV R3,R1,R2)
N
PC=0x0C(DMUL R4,R4,R2)
Y
R4 42
ROB3, 42
ROB1
6
0
7
14
ROB4
4 DADD 42, 14
PC=0x10(DADD R4,R4,R1)
R4
N
multipliers
1 DIVD 14, 7
3 DMUL 6, 7
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 17: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 17:
DADD writes to CDB,
ROB gets value, but
register file not updated
branch
N
-
BEQZ ROB1,Loop
Y
R4 42
ROB4, 56
ROB1
6
0
7
14
ROB4
Y
multipliers
R4 56
PC=0x00(DIV R3,R1,R2)
PC=0x0C(DMUL R4,R4,R2)
PC=0x10(DADD R4,R4,R1)
PC=0x04(BEQZ R3,Loop)
4 DADD 42, 14
1 DIVD 14, 7
N
N
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 18: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
R3
-
2
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
branch
N
-
BEQZ 2,Loop
Y
R4 42
ROB1, 2
ROB1
6
0
7
14
ROB4
Y
multipliers
R4 56
PC=0x00(DIV R3,R1,R2)
PC=0x0C(DMUL R4,R4,R2)
PC=0x10(DADD R4,R4,R1)
PC=0x04(BEQZ R3,Loop)
1 DIVD 14, 7
N
N
Cycle 105:
DIVD writes to CDB, ROB, BEQZ updated
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 19: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 106a:
Register R3 updated
(ROB1 released).
branch
N
-
Y
R4 42
6
2
7
14
Y
multipliers
R4 56
R3 2
PC=0x00(DIV R3,R1,R2)
PC=0x0C(DMUL R4,R4,R2)
PC=0x10(DADD R4,R4,R1)
PC=0x04(BEQZ R3,Loop)
BEQZ 2,Loop
Y
ROB4
ROB1
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 20: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 106b:
BEQZ executes, detects misprediction,
starts flush of ROB
branch
N
-
Y
R4 42
6
2
7
14
Y
multipliers
R4 56
flush
PC=0x0C(DMUL R4,R4,R2)
PC=0x10(DADD R4,R4,R1)
PC=0x04(BEQZ R3,Loop)
BEQZ 2,Loop
ROB4
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 21: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 107:
ROB flushed (may take more than one cycle), RAT reset, “front end” of pipeline fetches correct next instruction
branch
N
-
Y
R4 42
6
2
7
14
Y
multipliers
R4 56
flush
PC=0x0C(DMUL R4,R4,R2)
PC=0x10(DADD R4,R4,R1)
PC=0x04(BEQZ R3,Loop)
BEQZ 2,Loop
ROB4
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 22: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 109a:
DSUB issues: allocate ROB and reservation station entries, copy R4 and R2 values into reservation station, and …
branch
N
-
N
R4
6
2
7
14
multipliers
PC=0x08(DSUB R4,R4,R3)
PC=0x04(BEQZ R3,Loop)
BEQZ 2,Loop
4 DSUB 6, 2
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 23: Tomasulo With Reorder Buffer
adder
multipliers
Reservation
Stations
Intr.
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
-
Done?
Dest
Dest
Oldest
Newest
Reorder Buffer
R4
R3
R2
R1
Cycle 109b:
… updates RAT
branch
N
-
N
R4
6
2
7
14
multipliers
PC=0x08(DSUB R4,R4,R3)
PC=0x04(BEQZ R3,Loop)
BEQZ 2,Loop
4 DSUB 6, 2
ROB3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 24: Exceptions
So far, we have considered how to design hardware to support higher performance execution of a program, but we assumed we can always execute an instruction.
What happens if an instruction cannot complete or the program needs to ask the operating system to do something?
If there is a bug, the program might tell the hardware to do something that is impossible. For example, divide by zero, or read/write the wrong location in memory. Another reason an instruction might not be able to complete is related to virtual memory.
We call these “special cases” exceptions.
The hardware detects exceptions and has a special program run that either handles the exception, or passes control to the operating system. The OS may handle the exception or end the program.

## Slide 25: Exceptions
Exceptions are also sometimes referred to “interrupts”, or “faults”. We’ll just call them all “exceptions”.
Generally they require transfer of control to the operating system (OS) or other software “handler” routine.
Causes:
  I/O device request
  Invoking an OS service from a user program
  Page fault
  Memory protection violation
  FP arithmetic anomaly
  Integer arithmetic overflow
  etc...

## Slide 26: Categories of Exceptions
Synchronous versus Asynchronous
  Async: external device or hardware failure.
User requested versus coerced
  user requested => handle after instruction
User maskable versus user nonmaskable
  e.g., overflow can be masked (ignored) by user.
Within versus between instructions
  within => hard
Resume versus terminate
  terminate => easier
Most challenging, but very important =>
required for supporting “virtual memory”
(which we will talk about later).

## Slide 27: Exceptions in an In-order Pipeline
Upon detection of exception:
  Force first instruction of an exception handler upon next IF
  Turn off control signals for all instructions after and including “faulting instruction” (i.e., convert them to “nops” / “squash” them)
  After exception handling routine gets control, save PC of faulting instruction (or N+1 PCs if delayed branch with N delay slots)

## Slide 28: Exception Handling Support

## Slide 29: Exception Handling Support
add instruction causes overflow!
exception handler address
“nop”/“squash” injection signals
save PC of instruction causing fault, plus cause of fault
add instruction causes overflow!
save PC of instruction causing fault, plus cause of fault
exception handler address
“nop”/“squash” injection signals

## Slide 30: Exception Handling Support
First instruction of handler

## Slide 31: After exception handled...
RFE instruction restarts pipeline (MIPS)

## Slide 32: Precise Exceptions
If hardware guarantees that ALL instructions before faulting instruction have updated programmer visible state (i.e., R1...R31, memory) and NONE after (and including) faulting instruction have updated programmer visible state, then pipeline is said to support precise exceptions.
div
WB
IF
Has not updated “programmer visible state”
Has updated “programmer visible state”

## Slide 33: Precise Exceptions?
Both Scoreboard and Tomasulo have:
  In-order issue, out-of-order execution, out-of-order completion
Out-of-order completion means that interrupts are not precise
Need way to “resynchronize” execution with instruction stream
  Easiest way is with reorder buffer
18

## Slide 34: Memory Dependencies
)
Write
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[10]
<val4>
S.D F2,0(R3)
ADD.D F0,F2,F3
Y
Y
F3
M[10]
L.D F3,0(R3)
Y
--
BNE F1,<…>
N
F1
DIV.D F1,F2,F0
Y
Done?
Dest
Dest
Oldest
Newest
Read
Memory
Dest
Reorder Buffer
Registers
<val3>
F3
F2
F1
F0
<val1>
<val2>
What about memory
hazards???
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 35: Memory Disambiguation
Example: SD R5,0(R2) LD R6,0(R3)
If LD wants to read from a different location than the SD wants to write to, it is safe for the LD to read memory *before* the SD writes memory?
Is this useful? Yes! Turns out to be very useful in out-of-order processors (e.g., Core i7 tries to do this).
When can LD read memory? Naïve answer is that we are not allowed to start load until we know that address 0(R2)  0(R3). More details next slide.
More sophisticated answer (Andreas Moshovos, University of Toronto): “Predict” whether or not they are dependent (called “dependence prediction”) and use reorder buffer to fixup if we are wrong. We won’t talk more about this (I do talk about it in EECE 527).

## Slide 36: Hardware Support for Memory Disambiguation
Add “store queue” to keep track of all outstanding stores to memory, in program order.
  Keep track of address (when becomes available) and value (when becomes available)
  FIFO ordering: retire stores from this buffer in program order
When issuing a load, record current head of store queue (know which stores are ahead of you).
When have address for load, check store queue:
  If any store prior to load is waiting for its address, stall load.
  If load address matches earlier store address (associative lookup), then we have a memory-induced RAW hazard:
    store value available  return value
    store value not available  return ROB number of source
  Otherwise, send out request to memory
Stores modify memory during commit, which is “in order”, and this prevents WAR/WAW hazards through memory.

## Slide 37: Limits to Performance
Pipeline CPI = Ideal CPI
+ Structural stalls
+ Data hazard stalls
+ Control hazard stalls
Have looked at how to remove/reduce stalls: pipelining, forwarding, out-of-order execution, branch prediction, speculative execution.
Can we reduce “Ideal CPI”?
Ideal CPI limited by rate at which instructions issued: 1 per cycle.
Modern microprocessors can achieve CPI < 1 by issuing more than one instruction per cycle.
We will start to speak about average instructions per cycle (IPC)
IPC = (1/CPI)

## Slide 38: Multiple Instruction Issue
We will just call it “multiple issue”
Two types of multiple issue processor
  Superscalar
    Dynamic issue - varying number of instructions per cycle.
    Statically or dynamically scheduled execution order
      i.e., in order, out of order w/ or w/o speculative execution
  VLIW (very long instruction word)
    Static issue - fixed number of instructions per cycle.
    Statically scheduled execution

## Slide 39: Inorder Superscalar Pipeline
3-wide Superscalar 486 Pentium
(2-wide superscalar)

## Slide 40: Statically Scheduled Superscalar
Issue up to N instructions per cycle (where N is the “issue width” of the processor).
Issue: Check each instruction for hazards with earlier instructions in program order issued this cycle, as well as against all earlier instructions still in execution.
tgt
src1
src1
tgt
src1
src1
tgt
src1
src1
Program order
Above: Comparisons to avoid RAW, WAR, and WAW hazards
in a 3-wide in-order superscalar.

## Slide 41: 2-Issue In-order Superscalar
Issue restriction: At most one Integer and one Floating Point operation can issue per cycle (this organization was used in the HP 7100 processor).
Challenge maintaining peak throughput: Next 3 instructions cannot use result of load; branch delay 4-5 instructions (if resolve in execute).
WB
EX
EX
EX
ID
IF
FP instruction
WB
MEM
EX
ID
IF
integer instruction
WB
EX
EX
EX
ID
IF
FP instruction
WB
MEM
EX
ID
IF
integer instruction
WB
EX
EX
EX
ID
IF
FP instruction
WB
MEM
EX
ID
IF
integer instruction
8
7
6
5
4
3
2
1
Clock Number

## Slide 42: Very Long Instruction Word (VLIW)
In a superscalar processor, we need to check for dependencies between instructions before they can be issued in parallel.
Each time we fetch and decode the same group of instructions we will find the same dependencies (through registers).
Why not let the compiler search for these dependencies and groups of instructions that are known to be independent? This is how a VLIW processor works
Drawbacks:
  Need to explicitly encode “no ops” for units that do not have an operation.
  Hard to predict which memory access instructions miss in cache
  Need to use profile feedback to find “hot traces” in program to extract instruction level parallelism
  Memory dependencies hard to determine in compiler
Inst N: ADD.D F1,F1,F4 NOP L.D F7, 0(R1) DSUBI R2,R2,#1 NOP
Inst N+1: ADD.D F1,F1,F7 MUL.D F4,F5,F6 NOP DSUBI R2,R2,#1 BEQZ R2, Loop

## Slide 43: Multiple Issue w/ Dynamic Scheduling
Use extension of Tomasulo’s algorithm.
Benefits:
  Overcome data hazards
  Overcome issue restrictions
Key challenge: for each instruction in issue packet, in program order
  Assign reservation station and update pipeline control tables
Two approaches to overcome this challenge:
  Run this step at higher clock frequency (i.e., do in half a clock cycle for 2-wide superscalar)
  Add logic to perform operation on multiple (e.g., 2) instructions at once.

## Slide 44: Tomasulo Organization (with two-wide issue)
44
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus 1‏
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
Common Data Bus 2‏
2x / cycle
Notes: 44
Resolve RAW memory conflict? (address in memory buffers)‏
Integer unit executes in parallel

## Slide 45: Example
Loop: L.D F0,0(R1) ; F0-array element
ADD.D F4,F0,F2 ; add scalar in F2
S.D F4,0(F1) ; store result
DADDIU R1,R1,#-8 ; decrement pointer 8 bytes (per DW)
BNE R1,R2,Loop ; branch R1 != R2
Assumptions:
2-wide issue
Infinite number of reservation stations
Perfect branch prediction (let’s do three iterations of loop); separate branch unit.
Issue instruction from target of taken branch 1 cycle after branch (due to fetch restrictions)
One Integer Unit (handles load/store effective address calculation)
Separate FP Function Unit for each type of FP operation
Issue and Write Results take one cycle
Latencies: One cycle for integer ALU; two cycles for loads; three cycles for FP adds
Two CDBs
Load/Store effective address calculation “decoupled” from memory access (e.g., compute effective address as soon as possible, even if data to store to memory is not available)
NO Reorder Buffer

## Slide 46: Example: 2-issue w/ Tomasulo
Fetch Issue 15 instructions/9 cycles = 1.67 IPC
Execution Completion rate = 15 inst./16 cycles = 0.94 IPC (much less than 2)
Mark relevant dependencies (true deps)
Each clock cycle: Start from oldest instruction, working toward younger instructions and attempt to apply scheduling algorithm + assumptions

## Slide 47: Modified Example (extra Int ALU)
Loop: L.D F0,0(R1) ; F0-array element
ADD.D F4,F0,F2 ; add scalar in F2
S.D F4,0(F1) ; store result
DADDIU R1,R1,#-8 ; decrement pointer 8 bytes (per DW)
BNE R1,R2,Loop ; branch R1 != R2
Changed Assumptions:
…
Address Adder & Integer Unit
…

## Slide 48: Modified Example, cont’d...
Execution completion rate: 3 cycles less (3/S.D vs 1/L.D: 16-4+1 = 13 vs. 16 cycles before) IPC = 15/13 = 1.15 (vs. 0.94)
Performance limited by waiting for branch to resolve.

## Slide 49: Modified Example, cont’d...
Execution completion rate: 3 cycles less (3/S.D vs 1/L.D: 16-4+1 = 13 vs. 16 cycles before) IPC = 15/13 = 1.15 (vs. 0.94)
Performance limited by waiting for branch to resolve.

## Slide 50: Example of Multiple Issue, Tomasulo & Reorder Buffer
Mark true dependencies
Each clock cycle: Start from oldest instruction, working toward younger instructions and attempt to apply <whichever OoO> algorithm rules
#8
#8
#8
Commit rate: 15 instructions in 14-5+1 = 10 cycle
Speculative execution helped use commit 1.5 instructions per cycle

## Slide 51: Summary of Slide Set 14
In this slide set, we learned about the following:
Support for precise exceptions and speculative execution
with a single mechanism: The reorder buffer.
Multiple issue lowers the “ideal CPI” to below 1.
Two forms of multiple issue: Superscalar, VLIW
We now know how a single processor “core” works. In the next slide set we will talk about software approaches to instruction scheduling, take a look at the Pentium 4 processor, and talk about the limits of instruction level parallelism.
After this we will shift focus to multicore processors. Note that while the current focus is on increasing the number of cores per chip, extracting greater levels of instruction level parallelism will remain important due to Amdahl’s Law.