## Slide 1: CPEN 411: Computer Architecture Slide Set #16: Branch Prediction
Tor Aamodt
aamodt@ece.ubc.ca
Background: Pentium 4 die photo (uses advanced branch prediction mechanisms)

## Slide 2
instruction
flow
register
data flow
memory
data flow
intercore
comms

## Slide 3: Intel Core i7
Execution Units
Out-of-Order Scheduling & Retirement
L2 Cache & Interrupt Servicing
Instruction Fetch & L1 Cache
Branch Prediction
Instruction Decode & Microcode
Paging
L1 Data Cache
Memory Ordering & Execution
Highlighted above: Significant investment of silicon area to “predict branches”.

## Slide 4: Introduction to Slide Set 16
In the past couple of slide sets we considered how to execute instructions “out-of-order”.
The key to out-of-order execution (with Tomasulo’s algorithm) is finding instructions which do not have true data dependencies.
Did not talk about how to handle branches: Branches limit number of instructions we can consider for dynamic scheduling.
In this slide set, we explore mechanisms for predicting the “outcome” of a branch long before executing the branch.
Requires a way to “recover” when the prediction is incorrect (our prediction techniques will be incorrect sometimes). Note, we already learned how to “recover” after incorrect predictions when using Tomasulo’s algorithm by using a reorder buffer.

## Slide 5: Learning Objectives
After we finish this set of slides you should be able to:
Describe the motivation for and purpose of a branch predictor and branch target buffer.
Explain why it is possible to predict branch outcomes with relatively good accuracy.
Describe three types of branch predictor and evaluate their operation in detail.

## Slide 6: Control Dependence (H&P 2.1)‏
Intuition: An instruction X is control dependent on a branch B if whether instruction X executes is determined by the outcome of branch B.
if( p1 ) {
S1; // S1 (statement 1) control dependent on p1
}
if (p2) {
S2; // S2 control dependent on p2, not c.d. on p1
}
Control dependencies lead to control hazards. Earlier, we saw three approaches to dealing with control hazards: (1) wait for the branch to execute, (2) “predict not taken” (3) delayed branches,. In this slide set, we extend the “predict not taken” approach.

## Slide 7: Control Hazards
Predict-not-taken. Expanded pipeline view, showing flushed instructions (assuming branch “resolved in execute”):
WB
MEM
ID
branch target (Label)
IF
WB
MEM
branch + 2 (PC+8)
WB
MEM
EX
ID
IF
branch +1 (PC+4)
WB
MEM
EX
ID
IF
BEQZ R1, Label
8
7
6
5
4
3
2
1
Clock Cycle
MEM
EX
ID
branch target. + 1
EX
ID
IF
branch target. + 2
IF
ID
EX
EX
IF
Clock cycle 1: IF stage predicts “branch+1” is the next instruction to fetch.
Clock cycle 3: EX stage resolves branch, instructions in ID (“branch+1”) and IF (“branch+2”) turned into “no-ops”… they are “flushed”, correct next instruction (“branch target”) fetched on clock cycle 4.
Taken Branch

## Slide 8: Branch Prediction Impact (5-stage pipeline) – Resolved in EX
WB
MEM
EX
ID
IF
branch target. + 2
WB
MEM
EX
ID
IF
branch target. + 1
WB
MEM
EX
ID
IF
branch target
WB
MEM
EX
ID
IF
taken branch
8
7
6
5
4
3
2
1
Clock Number
Correct Prediction
WB
MEM
EX
ID
IF
actual next inst.
nop
nop
nop
nop
IF
predicted next inst.+1
nop
nop
nop
ID
IF
predicted next inst.
WB
MEM
EX
ID
IF
taken branch
8
7
6
5
4
3
2
1
Clock Number
Incorrect Prediction

## Slide 9: Effect of Deeper Pipelining
Waiting for branch to be executed incurs large penalty (related to number of pipeline stages between fetch and execute). If we correctly predict branch outcome, this penalty is “hidden”.
If branch prediction is wrong, we still pay the large penalty. Thus, important to build predictors that mispredict rarely.
Large Penalty !!!
“typical” modern pipeline
(superpipelined stages)
“textbook” pipeline

## Slide 10: Branch Instructions: Two Problems
Problem 1: Is branch taken? (“direction”)
  Hardware to predict this: “Branch Predictor”
  We will look at several designs
Problem 2: If taken, what is target PC?
  Hardware to predict this: “Branch Target Buffer”
  We will look at one design that works fairly well.

## Slide 11: Branches Predicted in Fetch Stage
“Next PC” based upon *prediction* of branch outcome.
Branch- Target Buffer
Adder (+4)
Branch- Predictor
PC
Instr Mem
Branch Instruction
Fetch stage (IF)
Decode stage (ID)…
taken?
taken?
hit?
1
1
0
Two new hardware
structures:
1. Branch Target Buffer
2. Branch Predictor
Our focus:
What is the motivation?
What do they do?
How do we use them?
How do we design them?
Next PC
Quick Review: How are instructions fetched?
Recall, from Slide Set 8:

## Slide 12: Predicting the future...
Method #1
  Crystal ball!!
Method #2
  Study history since “history repeats itself”.
  This works amazingly well in computer architecture
  Past branch “behaviour” => excellent predictor of future branch “behaviour”.
(doesn’t work)

## Slide 13: Example Prediction Problem
Loop: ...
...
DSUBI R1,R1,#1
BNEZ R1,Loop ; taken 9 times, not taken once
Observations: For this code, last branch outcome (taken,
not taken) a good (but not perfect) predictor of next branch
outcome. This turns out to be true for many branches.

## Slide 14: design hardware to use observation?

## Slide 15: 1-Bit Branch Predictor
Use “n” lower order bits to select row from table.
2n x 1 bit table
Output (“0”) is previous actual outcome of branch:
“1” => last time this branch was “taken” (T)
“0” => last time, this branch was “not taken” (NT)
000000011
01…100
00
PC of branch
Row 002
Row 012
1
0
0
0
Row 102
Row 112
Row 2n-1
Choose “n” for good CPI/area trade-off (good “!/$”)
Notes: 1. How might we remember the last branch outcome? Answer: table with one bit per branch.
2. What does each bit in the table mean? Answer: last correct outcome.
3. What is a good way for hardware to identify individual branches? Answer: address of branch.
4. How might we use the instruction address to pick one of the entries in our table? Answer use some bits as an index.
5. Which bits should we use? Answer: n-bits where table size is 2^n, but discard lower 2 bits since instructions are 32-bits long and aligned in memory.
6. How do we pick the number of entries in our table? Answer: CPI – cycle time - area tradeoff.

## Slide 16: Operation of 1-bit Branch Predictor
Step 1: Making a Prediction:
  Take n-bits of “PC” and use it to select a row in table. If entry in that row is “1”, prediction is “taken” and if entry is “0”, prediction is “not taken”.
  PC here is address of the branch instruction itself.
Step 2: Updating Predictor
  When we know the correct outcome of the branch update the entry in the table to be “1” if the actual outcome was “taken”, and to “0” if the actual outcome was “not taken”

## Slide 17: Aside: Hash Tables
Some of you might have learned about “hash tables” in one of your programming courses. You might note that the hardware used for branch prediction does something similar. (If you don’t remember, don’t worry about it.)

## Slide 18: Example, cont’d
Loop: ...
...
DSUBI R1,R1,#1
BNEZ R1,Loop

## Slide 19: 1-bit Branch Predictor
N
Again when see loop again‏
TTTTTTTTTNTTT
T
Mispredicts last loop iteration
time (loop iteration)
Actual outcome: TTTTTTTTTNTTTTTTTTTNTTTT
Problem: A branch that is almost always taken (not-taken) will mispredict twice each time branch is not-taken (taken).
Predicted outcome:
?
TTTTTTTT

## Slide 20: ideas to get rid of mispredictions?

## Slide 21: 2-bit Branch Predictor
Observations:
  Repeating T stays in ‘11’ state
  Repeating NT stays in ‘00’ state
  Two-in-a-row to change prediction
    (T,NT) won’t change prediction
    (NT,T) won’t change prediction
T
11
T
10
NT
01
NT
00
T
NT
T
T
T
NT
NT
NT
Transitions determined by
actual outcome of branch
T= “Taken”/ NT=“not taken”
Current state provides
prediction:
T= “Taken”/ NT=“not taken”
State encoding uses
two bits (encoding
is arbitrary)

## Slide 22: 2-bit “Saturating Counter” Predictor
T
10
NT
00
NT
01
T
11
NT
T
T
NT
T
T
NT
NT
2-bit counter that is incremented
after a taken branch, and
decrement after a not-taken branch.
Prediction is simply most significant bit.

## Slide 23: 2-Bit Predictor
Size of table (in bits) =
2n x 2 (n=# of PC bits used)
0 0
1 0
1 1
Row 002
Row 012
Row 102
Row 112
Row 2n-1
000000001
01…100
00
PC of branch
Contents of each row specify state in state machine. Make prediction based upon current state. E.g., if in state “10”, saturating counter state machine says predict “taken”.
When actual branch outcome known, update entry in table. E.g.,
if actual outcome taken new state in row is “11”
T
10
NT
00
NT
01
T
11
NT
T
T
NT
T
T
NT
NT
prediction based
upon current state.
next state
depends upon
current state and
actual outcome.

## Slide 24: Other 2-bit predictors (there are 1000’s of possible 2-bit state machines...)
Study: Ravi Nair, IBM, 1992
Saturating 2-bit counter is close to “optimal” among all 2-bit
state machines (though we will see better predictors).

## Slide 25
Loop: ...
...
DSUBI R1,R1,#1
BNEZ R1,Loop
Assume branch is “taken” 9 times in a row then not taken (i.e., loop iterates 10 times before exiting).

## Slide 26: 3-bit “Saturating Counter” Predictor
T
100
NT
000
NT
001
NT
010
NT
011
T
111
T
110
T
101
NT
NT
T
T
T
NT
NT
NT
T
NT
NT
NT
T
Can increase to N-bits
(but diminishing returns
as N grows)

## Slide 27: Branch Prediction “FAQ”
Important: Branch predictor only makes predictions. Correct predictions NOT necessary for correct program execution. Correct predictions improve performance. Hardware must check if predictions were correct when branch is executed. If wrong, “throw out” instructions following branch and start fetching again.
Branch predictor used to reduce CPI (increase performance)
There is a trade off between predictor size (silicon area), and the accuracy of the predictor.
Significant innovation in branch predictor design 1985-2005.
Typically around 95% correct prediction rate on real programs with sophisticated predictor designs (1-bit predictor: ~70-80%)
Further improvements? Example: Going from 96% to 99% accuracy (factor of 4 fewer mispredictions) might uncover roughly twice as much instruction level parallelism in a typical program.

## Slide 28: Branch Target Buffer (BTB)
Many ways to perform “look up” operation
  Simplest is to use m bits of PC to select a single row to compare left hand side address against entire PC (this is called a “direct mapped” cache structure)
BTB is a form of cache
Predicted (target) PC of
branch or jump instruction
“tags”
“targets”

## Slide 29: Putting it all together: BP + BTB
Prediction from BP used to select new PC value
Not shown: Inputs to BTB and BP for training.
Branch- Target Buffer
Adder (+4)
Branch- Predictor
PC
Instr Mem
Instruction
We had Adder and Inst. Mem blocks already
Instruction fetch stage (IF)
decode stage (ID)…
taken?
branch
misprediction?
(from EX)
hit?
1
1
0
1
0
correct PC
(from EX)

## Slide 30: The curious case of function calls
problem:
return address
depends on where
print was called from
for (;;) {
...
print(...);
...
print(...);
...
print(...);
...
}
print(...) {
...
return;
}

## Slide 31: Return address stack
Special case for function call / return
  HW can distinguish these from other jumps (how?)
  jal / jalr / jr r31 in MIPS, call / ret in x86, ...
when we see a call:
push addr on stack
ret addr
ret addr
when we see a return:
pop addr from stack

## Slide 32: BTB Terminology
In some designs, the BTB is combined with the branch predictor. Often the combined hardware is also called a BTB (even though it corresponds to a BTB and a branch predictor).
This is not true in all designs
Some use “branch predictor” to mean BTB + branch predictor
H&P uses BTB to mean BTB + branch predictor
On 411 quiz/exam: BTB means only the part of the hardware that predicts the branch target, not whether the branch is taken.

## Slide 33: Another Branch Prediction Example…
MIPS64 Assembly
0000002 BNEZ R1,L1 ; branch b1 (d!=0)
0001002 DADDI R1,R0,#1 ; d=1
0010002 L1: DADDI R3,R1,#-1 ; R3 = d - 1
0011002 BNEZ R3,L2 ; branch b2 (d!=1)
...
1001002 L2:
consider initial values for d = 0, 1, 2:
C code
if (d==0) // b1
d=1;
if (d==1) { // b2
…
}
T
no
2
T
no
2
N
yes
1
T
no
1
N
yes
1
N
yes
0
b2
d==1?
value of d before b2
b1
d==0?
initial value of d
instruction addresses (binary)
g

## Slide 34: Example, cont’d...
N
N
T
N
N
T
0
T
N
T
new b2 prediction
T
N
T
T
N
2
N
T
N
N
T
0
T
N
T
T
N
2
b2 action
b2 prediction
new b1 prediction
b1 action
b1 prediction
d=?
First, let’s consider behavior of the simple 1-bit predictor from slide 14 (all table entries initialized to “not taken”) if d alternates from 2 to 0: d = 2, 0, 2, 0, ...
across: behavior as code executes a single time
down: successive passes through the example code
from previous slide
Always mispredicts!

## Slide 35: Another Example…
MIPS64 Assembly
0000002 BNEZ R1,L1 ; branch b1 (d!=0)
0001002 DADDI R1,R0,#1 ; d=1
0010002 L1: DADDI R3,R1,#-1 ; R3 = d - 1
0011002 BNEZ R3,L2 ; branch b2 (d!=1)
...
1001002 L2:
consider initial values for d = 0, 1, 2:
C code
if (d==0) // b1
d=1;
if (d==1) { // b2
…
}
T
no
2
T
no
2
N
yes
1
T
no
1
N
yes
1
N
yes
0
b2
d==1?
value of d before b2
b1
d==0?
initial value of d
instruction addresses (binary)
Note: branch b2 correlated with branch b1 (if b1 is T, likely b2 is T)
g

## Slide 36: Why Are Branch Outcomes Correlated? Answer: Affector Branches
x=0;
if( someCondition ) { /* branch A */
x=3;
}
if( someOtherCondition ) { /* branch B */
y += 19;
}
if( x <= 0 ) { /* branch C */
doSomething();
}

## Slide 37: A (Silly) Analogy…
Which bus route should you take to school tomorrow?
Goal is to get to school fastest.
Make prediction based upon:
  Static information (shortest bus route in km?)
  History: Most times, route T was faster than route N.
  Better prediction if consider additional “context”: Route N better than route T on rainy days, but worse on sunny days. Ask friend how roads were this morning?

## Slide 38: (Silly) Correlating Branch Predictor Analogy…
Problem: You want to predict which bus to take to school.
You have a feeling that the best route to take seems to depend on the weather. It rains 50% of the time and is sunny 50% of the time.
You don’t yet know it, but “route T” is usually faster than “route N” on sunny days, but is often slower than “route N” on rainy days. Perhaps there are lots of accidents on route T when it rains. You don’t care why the bus is slow, you just want to make it to class on time. Besides, you’re too busy studying while on the bus to notice why it is faster or slower.
How are you ever going to notice you should predict N on rainy days, and T on sunny days?
Solution: Keep two tables: One you record what happens on rainy days, other you record what happens on sunny days.

## Slide 39: 1-Bit Branch Predictor with1-Bit of Correlation:
Was prior branch “taken”?
no
yes
N
N
if (d!=0) goto L1
d=1;
L1: if (d!=1) goto L2
...
L2:
...
T
N
Row 002
Row 012
Row 102
Row 112
Row 2n-1
000000010
00…000
00
PC
Use prior branch outcomes to select which table to use. Prior branch outcome is like “checking weather” before deciding which bus to. After actual branch outcome is known, update entry used to make prediction with actual branch outcome information.

## Slide 40: 1-Bit Predictor with 1-Bit of Correlation:
Was most recent branch taken? (assume we start with
answer = “no” for first branch)
no
yes
NT
NT
if (d!=0) goto L1;//b1
d=1;
L1: if (d!=1) goto L2;//b2
...
L2:
...
NT
NT
pass 1: d=2
(predicting b1)

b1
Row 002
Row 012
Row 102
Row 112
Row 2n-1
000000000
00…000
00
PC
1-bit of “branch history” used to correlate prediction for current branch with outcome of last branch.

## Slide 41: 1-Bit Predictor with 1-Bit of Correlation:
NT
NT
if (d!=0) goto L1;//b1
d=1;
L1: if (d!=1) goto L2;//b2
...
L2:
...
T
NT
pass 1: d=2,
(after executing b1,
before executing b2)
b1
Row 002
Row 012
Row 102
Row 112
000000000
00…000
00
PC
Update table after
actual outcome of
b1 is known
Was most recent branch taken? (assume we start with
answer = “no” for first branch)
1-bit of “branch history” used to correlate prediction for current branch with outcome of last branch.
no
yes
Row 2n-1

## Slide 42: 1-Bit Predictor with 1-Bit of Correlation:
Was most recent branch taken? “Yes” because b1 was taken.
1-bit of “branch history” used to correlate prediction for current branch with outcome of last branch.
no
yes
Row 2n-1
NT
NT
if (d!=0) goto L1;//b1
d=1;
L1: if (d!=1) goto L2;//b2
...
L2:
...
T
NT
pass 1: d=2
(predicting b2)
b2
Row 002
Row 012
Row 102
Row 112
000000010
00…000
00
PC


## Slide 43: 1-Bit Predictor with 1-Bit of Correlation:
Was most recent branch taken? “Yes” because b1 was taken.
1-bit of “branch history” used to correlate prediction for current branch with outcome of last branch.
no
NT
T
if (d!=0) goto L1;//b1
d=1;
L1: if (d!=1) goto L2;//b2
...
L2:
...
T
NT
pass 1: d=2
(updating predictor
for b2)
b2
Row 002
Row 012
Row 102
Row 112
000000010
00…000
00
PC
yes

## Slide 44: Example, cont’d...
N/T
N
N/T
T/N
N
T/N
0
N/T
N/T
N/T
new b2 prediction
T
N/T
T/N
T
T/N
2
N
N/T
T/N
N
T/N
0
T
N/N
T/N
T
N/N
2
b2 action
b2 prediction
new b1 prediction
b1 action
b1 prediction
d=?
Consider behavior of a 1-bit predictor with one bit of correlation history... if d alternates from 2 to 0: d = 2, 0, 2, 0, ...
across: behavior as code executes a single time
down: successive passes through the example code
6 out of 8 = 75% correct predictions
from slide 29

## Slide 45: 2-bit Predictor with 1-bit of Correlation
Useful to build a predictor that uses both correlation and hysteresis.
PC
most recent
branch taken?
no
yes
n bits
1 0
0 1
0 0
1 1
1 0
0 0
2 x 2n x 2 bit table
T
10
NT
00
NT
01
T
11
NT
T
T
NT
T
T
NT
NT

## Slide 46: Affector Branches, reconsidered…
x=0;
if( someCondition ) { /* branch A */
x=3;
}
if( someOtherCondition ) { /* branch B */
y += 19;
}
if( x <= 0 ) { /* branch C */
doSomething();
}

## Slide 47: Correlating against Multiple Branches
In the last slide we saw that the outcome of branch C depended in some way upon the outcome of branch A but not Branch B.
Instead of tracking the outcome of only the last branch and using that to choose between two tables, we will track the outcome of last N branch outcomes and use that to choose between 2N tables.
We track the outcome of the last N branches using an N-bit shift register.

## Slide 48: Quick Review: Shift Register
Each cycle, shift contents of this register by one bit:
In Q1 Q2 Q3 Q4
cycle 0 1 0 0 0 0
cycle 1 0 1 0 0 0
cycle 2 1 0 1 0 0
cycle 3 1 1 0 1 0
cycle 4 0 1 1 0 1
cycle 5 0 0 1 1 0

## Slide 49: Increase “History Length” - gselect branch predictor (e.g., correlate against last 2 branches)
if( aa==2 )
aa=0;
if( bb==2 )
bb=0;
if( aa!=bb ) {
goal: want better
prediction for
this branch
Real code example from SPEC89
benchmark “eqnott”:
Global branch history = shift register (recall from 353) “Shift in” branch outcomes of earlier branches.
T
10
NT
00
NT
01
T
11
NT
T
T
NT
T
T
NT
NT

## Slide 50: Track outcome of 3-branches
Which is “correct” one to use?
T
100
NT
000
NT
001
NT
010
NT
011
T
111
T
110
T
101
NT
T
T
T
NT
NT
NT
T
NT
NT
NT
T

## Slide 51: gshare branch predictor
PC
GBHR
bitwise XOR
1 1
1 0
0 0
more history, exponentially more tables
  tradeoff between # tables vs # branches tracked
but long history required for useful correlation
pattern history table (PHT)
what are the tradeoffs?

## Slide 52: Remembering history
BHR
last branch outcome
BHR
branch history register
PHR
path history register
PHR 0
last branch target PC
xor
what are the tradeoffs?

## Slide 53: Kinds of branches
unconditional vs conditional — beqz vs j
direct (target known statically) — j LABEL
  for-loop end (j)
  simple function call (jal)
indirect — j [r5]
  function return (target known @ runtime)
  function pointer (when is target known?)
  virtual method call (runtime-type-dependent)

## Slide 54: Pentium M Branch Predictor
Intel/AMD tend not to disclose many details about their branch predictors
It is possible to infer structure of branch predictor using “microbenchmarks”.
The figure is from a recent academic paper. The authors determined this structure by running microbenchmarks on the Pentium M and using VTune.
Vladimir Uzelac, Aleksandar Milenkovic: Experiment flows and microbenchmarks for
reverse engineering of branch predictor structures. ISPASS 2009: 207-217

## Slide 55: Global (T/NT) predictor
is this gselect or gshare?

## Slide 56: BTB organization

## Slide 57: Predicting counted loops
long for-loops: best-case for 2-bit bimodal BP?
can we predict loops perfectly?
what would we have to learn?
  recognize it’s a counted loop
  find out max value
  track current value

## Slide 58: Loop Predictor

## Slide 59: Indirect branches
e.g., virtual function call (inheritance)
  animal *a;
  ...
  a->greet(“Whisky”);
  person::greet(name):
  say(“Hello”);
  say(name);
  cow::greet(name):
  say(“moo.”);
  say(“mooooooooooo!”);

## Slide 60: Predicting indirect branch target(s)
how to predict?
observation: often context is enough
(plot: Kim et al)

## Slide 61: Indirect BTB
how is iBTB different from BTB?

## Slide 62: More predictor ideas
several predictors + majority vote
several predictors + tournament predictor
train ML model (e.g., perceptron) instead of FSM
track path history instead of branch history
variable history length (maybe compiler chooses)
keep local history (BHT), alloy w/ GBHR
guess if predictor correct, invert if not
dataflow predictor (track affector branches)
what else can we predict?

## Slide 63: Summary of Slide Set 16
Branch prediction is motivated by need to keep pipeline filled with instructions. This is especially important for processors that use out-of-order execution and deep pipelines. It motivates significant investment of silicon area.
A 1-bit predictor uses the last outcome of a branch to predict the next outcome.
A 2-bit predictor uses a state machine. The current state indicates the prediction. The outcome determines the next state.
A correlating branch predictor uses information about other branch outcomes when making a prediction about the current branch.