## Slide 1: CPEN 411: Computer Architecture Slide Set #4: Instruction Set Architecture Design
Instructor: Tor Aamodt

## Slide 2: The RISC vs. CISC Debate
RISC = Reduced Instruction Set Computer
CISC = Complex Instruction Set Computer
Red portion on Pentium Pro represents overhead of supporting CISC (about 5% area increase)
PowerPC 620 - “RISC” ISA
PentiumPro - “CISC” ISA
(w/ “RISC implementation”)
Notes: This might have raised manufacture cost of Pentium Pro as much as 15% assuming defect density of 1.5/cm^2, pentium pro chip area of 197 mm^2, and wafer cost of $1500 for a 200mm dia wafer...

## Slide 3: Instruction Set Architecture (ISA)
The low-level software interface to the computer
  Language the computer understands
  Must translate any programming language into this language
  Examples: ARM, x86, PowerPC, MIPS, SPARC, …
ISA is the set of features “visible to programmer”
instruction set
software
hardware

## Slide 4: Levels of Representation
High Level Language Program
Assembly Language Program
Machine Language Program
Control Signal Specification
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
LW R15,0(R2)
LW R16,4(R2)
SW R16,0(R2)
SW R15,4(R2)
1000 1100 0110 0010 0000 0000 0000 0000
1000 1100 1111 0010 0000 0000 0000 0100
1010 1100 1111 0010 0000 0000 0000 0000
1010 1100 0110 0010 0000 0000 0000 0100
°
°
ALUOP[0:3] ← InstrReg[9:12] & MASK

## Slide 5: Elements of an ISA
Set of machine-recognized data types
  bytes, words, integers, floating point, strings, . . .
Operations performed on those data types
  Add, sub, mul, div, xor, move, ….
Programmable storage
  Registers, program counter, memory
Methods of identifying and obtaining data referenced by instructions (addressing modes)
  Addressing modes: Literal, register, absolute, relative, reg + offset, …
  Endianness, alignment restrictions
Format (encoding) of the instructions
  Op code, operand fields, …
Current Logical State
of the Machine
Next Logical State
of the Machine

## Slide 6: Four ISA Classes
Notes: First distinction among different ISAs: Type of internal storage.
Stack, Accumulator, or Register.
Stack used for x86 floating point instructions, Java byte code.
Accumulator: Very popular in digital signal processors.
Register Memory: 68000
Register-Register/Load-Store: MIPS, PowerPC, SPARC.
What are the tradeoffs?
Stack / Accumulator can use “implicit operands” => can improve code density. Important when memory is relatively expensive.
Other benefits of implicit operands? What about implementation? May require less area per bit of memory. May be faster (clock frequency).
Stack Drawbacks: Cannot access operands “hidden” on stack => compiler may need to generate longer instruction sequences.
Accumulator Drawbacks: Code generation is complicated. One operand is not equivalent to the other (it gets overwritten).
Benefits of Registers: Fast access to temporary variables => reduce traffic between memory and processor.

## Slide 7: Four ISA Classes
Stack
Push A
Push B
Add
Pop C
Accumulator
Load A
Add B
Store C
Reg/Mem
Load R1,A
Add R3,R1,B
Store R3,C
Reg/Reg
Load R1,A
Load R2,B
Add R3,R1,R2
Store R3,C
How to compute “C = A + B”:

## Slide 8: Question
Assume A, B, and C reside in memory. Assume opcodes are 8-bits. Memory addresses are 64-bits, and register addresses are 6-bits (64 registers)
For each class of ISA, how many addresses or names appear in each instruction for the code to compute C = A + B, and what is the total code size?

## Slide 9: Four ISA Classes
Stack
Push A
Push B
Add
Pop C
Accumulator
Load A
Add B
Store C
Reg/Mem
Load R1,A
Add R3,R1,B
Store R3,C
Reg/Reg
Load R1,A
Load R2,B
Add R3,R1,R2
Store R3,C
Stack 3 addresses, total bits = 4*8+3*64 = 224 bits
Accumulator 3 addresses, total bits = 3*(8+64) = 216 bits
Reg/Mem 3 addresses+4 regs, total bits = 3*64+4*6+3*8 = 240 bits
Reg/Reg 3 addresses+6 regs, total bits = 3*64+6*6+4*8 = 260 bits

## Slide 10: Trade-Offs
Stack
  extra code / memory bandwidth
  hard to “reorder” instructions
  + good code density
Accumulator
  difficult for compiler
  extra code / memory bandwidth
  + good code density
Register-Memory
  # of registers may be limited
  operands not equivalent
  + good code density
Register-Register
  - poor code density (more instructions to do same thing)
  + easy to pipeline
  + easy for compiler to generate efficient code

## Slide 11: Addressing Modes
Recall Notation:
  “Regs” is array of N-bit registers
    (for MIPS64, 32x64-bit registers)
    Regs[x] is the 64-bit quantity in register “x”
  “Mem” is array of bytes
    Mem[x] is “m” bytes starting at address “x”
    “m” will be implied by usage
Terminology:
  “Effective Address” = actual memory address calculated by instruction (just before accessing memory).

## Slide 12: Addressing Modes
  Mode Example Meaning
  Register Add R4,R3 Regs[R4] <- Regs[R4] + Regs[R3]
  Immediate Add R4,#3 Regs[R4] <- Regs[R4] + 3
  Displacement Add R4,100(R1) Regs[R4] <- Regs[R4] + Mem[ 100 + Regs[R1] ]
  Register Indirect Add R4,(R1) Regs[R4] <- Regs[R4] + Mem[Reg[R1]]
  Indexed Add R3,(R1+R2) Regs[R3] <- Regs[R3] + Mem[Regs[R1]+Regs[R2]]

## Slide 13: Addressing Modes
Mode
  Direct Add R1,(1001) Regs[R1] <- Regs[R1] + Mem[1001]
  Memory Indirect Add R1,@(R3) Regs[R1] <- Regs[R1] + Mem[Mem[Regs[R3]]]
  Autoincrement Add R1,(R2)+ Regs[R1] <- Regs[R1]+Mem[Regs[R2]] Regs[R2] <- Regs[R2] + d
  Autodecrement Add R1,-(R2) Regs[R2] <- Regs[R2] - d Regs[R1] <- Regs[R1]+Mem[Regs[R2]]
  Scaled Add R1,100(R2)[R3] Regs[R1] <- Regs[R1] + Mem[100+Regs[R2]+Regs[R3]*d]

## Slide 14: Addressing Modes
Lesson: ‘fancy’ addressing modes not used much by compiler
simple addressing modes used most often

## Slide 15: Displacement Mode
How many bits should be used to encode displacement?
What are the tradeoffs?

## Slide 16: Example: How Many Bits?
Imagine a RISC instruction set that supports a 24-bit displacement field and that initially Regs[R1]=0x40. We have a program with the following instruction:
LD R2, 0x10002(R1) ; Eff. Addr. = 0x10002+0x40=0x10042
NOTE: The value 0x10002 requires at least 17 bits to represent.
We can implement the same operation using a16-bit displacement by using multiple instructions. For example, using MIPS64 (which has a 16-bit displacement field):
LUI R3,#1 ; Regs[R3] = 0x10000
DADD R4,R3,R1 ; Regs[R4] = 0x10000+0x40=0x10040
LD R2,2(R4) ; Eff. Addr = 0x10040+0x2=0x10042

## Slide 17
Data Movement
Load (from memory)
Store (to memory)
memory-to-memory move
register-to-register move
input (from I/O device)
output (to I/O device)
push, pop (to/from stack)
Arithmetic
integer (binary + decimal) or FP
Add, Subtract, Multiply, Divide
Logical
not, and, or, set, clear
Shift
shift left/right, rotate left/right
Control (Jump/Branch)
unconditional, conditional
Subroutine Linkage
call, return
Interrupt
trap, return
Synchronization
test & set (atomic read-modify-write)
Typical ISA Operations
There are several basic types of operations that are found
in most instruction sets. These are listed below.

## Slide 18: Top 10 IA-32 Instructions
Rank
Instruction
Integer Average (Percent total executed)
1
load
22%
2
conditional branch
20%
3
compare
16%
4
store
12%
5
add
8%
6
and
6%
7
sub
5%
8
move register-register
4%
9
call
1%
10
return
1%
Total
96%
Simple instructions dominate instruction frequency

## Slide 19: Encoding an ISA
One important question is whether instructions are all encoded with the same number of bits. The options are “variable” encoding (each instruction can be a different size); “fixed” encoding (all instruction same), or a “hybrid” (where there may be a limited number of instruction sizes).
Choice influenced by competing forces:
  desire to have large # of registers + addressing modes
  code density
  ease of decoding
Once we decide which instructions we want, we need to specify the instruction in 1’s and 0’s so that digital logic gates can implement it. This is known as “encoding” the instruction set.

## Slide 20: Optimizing Compilers (e.g., “gcc -O3”)
Register allocation works best with >= 16 registers.
Orthogonal ISA features => compiler easier to write.
An optimizing compiler transforms code to make your software run faster. One important transformation is to allocate variables to registers. The number of registers impacts the effectiveness of optimizing compilers.

## Slide 21: Impact of Compiler Optimization
An important pitfall to avoid is optimizing a hardware design using software
benchmarks that have not been optimized by an optimizing compiler. The
data below shows how some characteristics of a program likely to be of
importance to an ISA designer can change dramatically before/after using
an optimizing compiler.

## Slide 22: Putting it all together: Desirable ISA Properties...
Local Storage
  general purpose registers (load-store architecture)
  at least 16 registers
Addressing Modes
  Displacement (12-16 bits)
  Immediate (8-16 bits)
  Register Indirect
Aligned memory accesses
Type and Size of Operands
  - 8-, 16-, 32-, and 64-bit integers, 64-bit FP
Minimalist instruction set: Simple operations used most frequently in practice (load, store, add, sub, move, shift, …)

## Slide 23: Desirable ISA Properties, Cont’d
PC-relative branches with compare equal, not-equal, less-than
Support function calls (PC-relative, indirect), returns
Fixed instruction encoding for performance, variable encoding for code density.
Provide at least 16 general-purpose registers.
Addressing modes apply to all data transfer instructions.