## Slide 1: CPEN 411: Computer Architecture Virtual Memory

## Slide 2: Learning Objectives
define and motivate virtual memory
describe how page tables implement VM
perform virtual  physical address translation
motivate and emulate the TLB
explain/address VM–cache interaction issues

## Slide 3: Virtual memory
problem: OS wants to multitask (time-multiplex)
  but all programs assume address space starts at 0
  enough physical RAM to run one program but not enough to fit all of them at once
solution: separate address space per program
  each program has separate address space ID (ASID)
  program executes using virtual addresses (VA)
  CPU + OS translate to physical addresses (PA)
  {ASID 42, VA 0xdeadbeef} ≠ {ASID 17, VA 0xdeadbeef} (they will map to different physical addresses)

## Slide 4: Multiple Programs Using Memory
OS starts, reserves some memory
browser starts, wants memory
Word starts, wants memory
open webpage, browser allocs memory
open doc, Word allocs memory
open webpage, browser allocs more
user edits doc, Word allocs more
total more than physical memory
Main
Mem
OS
Web
Word
Web
Web
Word
Word

## Slide 5: Fragmentation
Main
Mem
OS
Web
Web
Web
“writer’s block,” user exits Word (sorry ENGL 112)
start game, needs lots of RAM
and it wants contiguous addrs
can’t move the browser (has pointers to green memory)
Word
Word
Word

## Slide 6: Paged virtual memory
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
e
s
D
i
s
k
a
d
d
r
e
s
s
e
s
V
i
r
t
u
a
l
a
d
d
r
e
s
s
e
s
A
d
d
r
e
s
s
t
r
a
n
s
l
a
t
i
o
n
program view of memory
main memory, actually
nice contiguous address space, can always alloc more
pages
fragmented:
non-contiguous (holes), out-of-order, some on disk (that CPEN 411 sim...)
equal
size
pages

## Slide 7: Address Translation
3
2
1
0
1
1
1
0
9
8
1
5
1
4
1
3
1
2
3
1
3
0
2
9
2
8
2
7
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
3
2
1
0
1
1
1
0
9
8
1
5
1
4
1
3
1
2
2
9
2
8
2
7
P
a
g
e
o
f
f
s
e
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
T
r
a
n
s
l
a
t
i
o
n

## Slide 8: Page Table
D
i
s
k
a
d
d
r
e
s
s
e
s
civ
civ
civ
civ
civ
civ
civ
civ
program view
main memory view
Page Table
Virtual Addresses
Physical Addresses
Address Translation
civ
pages

## Slide 9: Page Table Translation Structure
page table register
2
0
1
2
1
8
3
1
3
0
2
9
2
8
2
7
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
2
9
2
8
2
7
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
virtual address
page offset
virtual page number
physical page number
physical address
physical page number
page offset
page table
valid?
if 0 then page is on disk
register
in CPU
per process:
changes
on OS
context
switch
2
7

## Slide 10: Where to put the page table?
option 1: on-chip near the CPU (like the L1$)
  pros: very fast access
  cons: 1 M entries >> any reasonable L1$
option 2: off-chip in main memory
  pros: might actually fit
  cons: access very slow (but must be done up to 2× per instr)
  cons: per-process tables still lots of memory

## Slide 11: Efficient Page Table Storage
P1 index
P2 index
page offset
31
12
11
0
21
22
32 bit virtual address
observation: each process needs own page table
  100s–1000s processes could easily be active
observation: page tables are sparse
  few programs use the entire address space
solution: multi-level PTs
  top-level table in RAM
  next-level either in RAM or paged out to disk

## Slide 12: So what’s in a PTE?
dirty
accessed
usermode
global
reserved
executable
writeable
readable
valid
XWR=0  pointer to next level PT
RISCV-32, Sv32 mode:
RISCV-64, Sv39 and Sv48:

## Slide 13: Translation-related exceptions
page fault
  page is accessible, but it’s sitting on disk
  this is not a program error!
  resume instruction execution once page in RAM
segmentation fault / general protection fault
  page is not user-accessible
  page is R/O but tried to write/exec
  program terminated (unless caught)
  Meltdown avoided this by misspeculating

## Slide 14: Faster page table access
okies, so page table stays in main memory
problem: access still. way. too. slow.
Q: how to speed up page table access?
cache it!
we’ll call this the translation cache
translation lookaside buffer (TLB)

## Slide 15: TLB: Translation Lookaside Buffer
1
1
1
1
0
1
1
0
1
1
0
1
1
1
1
1
0
1
TLB: a $ for the PT
page table
tag
physical page number
V
V
Physical Page Number or Disk Address
Physical Memory
Disk
virtual page number

## Slide 16: Writes and evictions
+ permission bits (read-only, execute), sharing info, etc.

## Slide 17: I$ access w/ address translation
V
a
l
i
d
T
a
g
D
a
t
a
P
a
g
e
o
f
f
s
e
t
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
V
a
l
i
d
1
2
2
0
2
0
1
6
1
4
C
a
c
h
e
i
n
d
e
x
3
2
C
a
c
h
e
D
a
t
a
C
a
c
h
e
h
i
t
2
B
y
t
e
o
f
f
s
e
t
D
i
r
t
y
T
a
g
T
L
B
h
i
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
t
a
g
T
L
B
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
3
1
3
0
2
9
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
1. ITLB lookup
3. access I$
2. translate VA to PA
Q: how many cycles?

## Slide 18: When to do address translation?
CPU
TLB
$
MEM
VA
PA
PA
physically
addressed
cache
CPU
$
TLB
MEM
VA
PA
tags
PA
overlap $ access
with VA translation
L2 $
CPU
$
TLB
MEM
VA
VA
PA
VA
tags
virtually
addressed
cache

## Slide 19: Virtually addressed L1 caches
...what must happen on a context switch?
misses because of flushing VA L1 caches

## Slide 20: Virtually addressed L1 caches
okies, so use {ASID, VA} to address L1 D$?
what if a memory region is shared among different processes (and so diff. ASIDs)?
problem: same page in D$ multiple times
what if we want to write to one of them?

## Slide 21: Overlapping TLB & L1 D$ accessses
Valid
Cache Tags
Cache Data
data out
Virtual Page Number | Page Offset
TLB
Virtual
Physical
=
hit?
cache tag
 | Index | Byte Select
Cache Block
Cache Block

## Slide 22: Virtually addr’d, physically tagged $
problem: some address bits change (VAPA)
but we need those bits to index the cache!
possible solutions
  bigger page sizes (8 KB in this case)
  more associativity (2-way set-associative here)
  OS guarantees VA[13] == PA[13] (harder if many bits)
  bite the bullet and deal w/ the synonym problem
7
6
offs
virt page #
offset
20
12
$ idx
bit changed by VAPA
but needed to index D$

## Slide 23: Synonym problem: example
64 KB direct-mapped $, 16-byte blocks
  block offset: addr[3:0]
  cache index: addr[15:4]
4 KB pages
  page offset: addr[11:0]
16 synonym locations for each PA
  4 virtual bits used to index $: addr[15:12]:
    process 1 VA 0x0000 000 0 -> PA 0xFF000000
    process 2 VA 0x0000 F00 0 -> PA 0xFF000000
    process 1 index = 0x000 (tag = 0xFF000)
    process 2 index = 0xF00 (tag = 0xFF000)
    what if process 1 writes, process 2 reads?

## Slide 24
ARM Cortex A53
(data path)

## Slide 25
Intel Core i7
(everything)

## Slide 26: Updating PTEs
when updating PTEs, what needs to be done?
synchronize PTE writes w/ addr translation HW
  flush any translation caches (TLBs)
  in multicores, also remote TLBs (TLB shootdown)
implementation options?
  instruction in fault handler, e.g., sfence.vma
  detect write to PT in HW, trigger TLB shootdown

## Slide 27: Summary
Why virtual addressing?
Page tables and VAPA translation
TLB = a cache for the page table
Virtually addressed, physically tagged cache
The synonym problem