## Slide 1: CPEN 411: Computer Architecture Slide Set #17: Memory Consistency
Tor Aamodt
aamodt@ece.ubc.ca

## Slide 2: Introduction to Slide Set 17
Writing correct software for a shared memory computer requires some understanding of how updates to memory made by one thread can be seen by other threads.
X86 hardware behaves “mostly” as you would expect, but there are some “corner cases” that might be surprising.
Other popular architectures such as ARM and PowerPC can provide even more surprising results to naive programmers.

## Slide 3: Learning Objectives
By the time we finish talking about this slide set in lectures you should be able to:
  Define sequential consistency.
  Evaluate memory orderings allowed by the TSO/x86 memory model.
  Explain how TSO or more relaxed consistency models differs from sequential consistency.
  Explain what a fence operation is and why it is necessary.
  Define what is meant by a data race
  Define sequential consistency for data race free programs

## Slide 4: Example #1
Core C1 | Core C2 | Comments
S1: Store data=NEW |  | // Initially data=0, // flag != SET
S2: Store flag=SET | L1: Load r1=flag | // L1 and B1 may
 | B1: if( r1!=SET ) goto L1; | // iterate many times
 | L2: Load r2=data | 
Can r2 get value other than NEW?
Potential scenarios:
C1 and C2 have non-FIFO store buffer, S1 misses and S2 hits
L2 executed before L1 (out-of-order execution with speculation)

## Slide 5: Example #2 (e.g., Dekker)
Core C1 | Core C2 | Comments
S1: x=NEW | S2: y=NEW | // Initially x=y=0
L1: r1=y | L2: r2=x | 
This last result can happen on x86 processors from Intel and AMD due to their use of write buffering to enhance performance.
What are “legal” outcomes after above code executes?
(r1, r2) = (0, NEW) for execution S1, L1, S2, then L2
(r1, r2) = (NEW, 0) for S2, L2, S1, and L1
(r1, r2) = (NEW, NEW), e.g., for S1, S2, L1, and L2
How about following? Is this a legal outcome?
(r1, r2) = (0, 0)

## Slide 6: Consistency Model
Memory consistency model specifies allowable orderings of loads and stores to different locations (e.g., x and y last slide)
The number of allowable execution orderings generally far greater than one.
Ordering of operations from different processors is non-deterministic. Software must use synchronization (mutexes, semaphores, etc…) to provide determinism.

## Slide 7: Sequential Consistency
Sequential consistency is basically a “naïve” programmer’s intuition of allowable orderings:
Notes: Also, multitasking uniprocessor

## Slide 8: Sequential Consistency
A multiprocessor is sequentially consistent if the result of any execution is the same as if the operations of all the processors were executed in some sequence, and the operations of each individual processor appear in this sequence in the order specified by its program (Lamport)
Note: Parallelism still possible (many interleaving orders are equivalent).

## Slide 9: Memory Order
Single writer multiple reader (SWMR) restriction implies all memory operations can be placed into a global “memory order”
Consistency can then be defined in terms of relationship of “program order” to “memory order”

## Slide 10: Example #1, Revisited
Sequential Consistent memory ordering
Program order of core C1
Memory order
Program order of core C2
L1: r1=flag /* 0 */
S1: data=NEW /* NEW */
L1: r1=flag /* 0 */
L1: r1=flag /* 0 */
S2: flag=SET /* SET */
L1: r1=flag /* SET */
L2: r2=data /* NEW */

## Slide 11: SC Ordering Rules
Operations from a single thread must respect following orderings when placed into memory order:
Load -> Load
Load -> Store
Store -> Store
Store -> Load

## Slide 12: Example #2, Revisited
Example of Non-SC execution:
Program order of core C1
Memory order
Program order of core C2
S2: y=NEW /* NEW */
S1: x=NEW /* NEW */
L2: r2=x /* 0 */
L1: r1=y /* 0 */
S2 and L2 violate “Store -> Load” ordering rule.

## Slide 13: Example #1, Revisited
Core C1 | Core C2 | Comments
S1: Store data=NEW |  | // Initially data=0, // flag != SET
S2: Store flag=SET | L1: Load r1=flag | // L1 and B1 may
 | B1: if( r1!=SET ) goto L1; | // iterate many times
 | L2: Load r2=data | 

## Slide 14: Example #2, Revisited
Core C1 | Core C2 | Comments
S1: x=NEW | S2: y=NEW | // Initially x=y=0
L1: r1=y | L2: r2=x | 

## Slide 15
Recall: Stores update memory at commit stage for Tomasulo with reorder buffer.
Problem: Store miss stalls commit.
Solution: Avoid stall by storing into a FIFO write buffer like we saw for write through cache.
Impact on consistency model?

## Slide 16: Write Buffer, Revisited
Q. Why a write buffer ?
Processor
Cache
Write Buffer
Lower Level Memory
Holds data awaiting write to coherent cache
A. So CPU doesn’t stall
Q. Why a buffer, why not just one register ?
A. Bursts of writes are
common.
Q. Are Read After Write (RAW) hazards an issue for write buffer?
A. Yes! Drain buffer before next read, or send read after 1st checking write buffers (stall or bypass value if match found)

## Slide 17: Total Store Order (TSO/x86) Memory Model
Use of write (store) buffer considered very important by Intel and AMD for x86.
Leads to total store order memory model supported by x86.
In general, memory model on multicore processors is not sequential consistency.

## Slide 18: TSO/x86 Ordering Rules
Operations from a single thread must respect following orderings when placed into memory order:
Load -> Load
Load -> Store
Store -> Store
Store -> Load : TSO/x86 allow loads to appear before prior store in memory order to enable write buffer in each core

## Slide 19: Example #1, Revisited
Core C1 | Core C2 | Comments
S1: Store data=NEW |  | // Initially data=0, // flag != SET
S2: Store flag=SET | L1: Load r1=flag | // L1 and B1 may
 | B1: if( r1!=SET ) goto L1; | // iterate many times
 | L2: Load r2=data | 

## Slide 20: Example #2, Revisited
Core C1 | Core C2 | Comments
S1: x=NEW | S2: y=NEW | // Initially x=y=0
L1: r1=y | L2: r2=x | 

## Slide 21: Example #2, TSO/x86 ordering
Program order of core C1
Memory order
Program order of core C2
S2: y=NEW /* NEW */
S1: x=NEW /* NEW */
L2: r2=x /* 0 */
L1: r1=y /* 0 */
(r1, r2) = (0, 0) is legal outcome under TSO/x86 (!)

## Slide 22: Fence Operations
Hardware provides ISA support to enable intended execution of code in Example #2.
Fence instruction ensures prior memory operations inserted into memory order before subsequent memory operations. E.g., for TSO require:
Store -> Fence
Fence -> Load

## Slide 23: Example #2, Revisited
Core C1 | Core C2 | Comments
S1: x=NEW | S2: y=NEW | // Initially x=y=0
F1: Fence | F2: Fence | 
L1: r1=y | L2: r2=x | 

## Slide 24: Relaxed Memory Consistency
PowerPC, ARM increase performance by enforcing memory ordering ONLY when programmer asks for it explicitly
Require fence operations to enforce most ordering

## Slide 25: Related: Write atomicity
When performing a store does new value become visible to all other threads at same time?
Yes: called write atomicity (or store atomicity)
PowerPC & ARM: Do not enforce write atomicity (breaks SWMR assumption)

## Slide 26: Example 3: Causality
Causality: “If I see it and tell you about it, then you see it too.”
Programmer’s intuition about causality (“Print A” displays “1”) may be violated on a system lacking write atomicity
P
1
P
2
/* Assume initial value of A and B are 0 */
A = 1;
while (A == 0);
/*spin wait */
B = 1;
P
3
while (B == 0);
Print A;
(message
delay
for A)

## Slide 27: When do we need fences?
Typically, programmer uses “synchronization” to protect accesses to shared data.
E.g., critical section
aquire(mutex) // synchronization
modify shared data
release(mutex) // synchronization

## Slide 28: Data Races
Data race: Two or more threads accessing same data with one thread writing and no synchronization between accesses

## Slide 29: SC for DRF Programs
Fact: All memory consistency models support sequential consistency for programs free of data races.
Avoid needing to worry about hardware consistency model if you use correct synchronization (e.g., mutex)