## Slide 1: CPEN 411: Computer Architecture Slide Set #18: Cache Coherence (Part 1)
Tor Aamodt
aamodt@ece.ubc.ca

## Slide 2: Introduction to Slide Set 18
In the prior slide set we considered memory consistency or the order that memory accesses to multiple locations from one thread may become visible to another thread running on a different processor.
In this slide we consider cache coherence or how an update to a single location on one core becomes visible to threads running on a different core.

## Slide 3: Learning Objectives
By the time we finish talking about this slide set in lectures you should be able to:
  Describe the snoop based approach to implementing shared memory.
  Evaluate which events are generated when loads and stores operate with a simple snoop cache coherence protocol for writeback caches.
  Describe how a directory based cache coherence protocol differs from a snooping cache coherence protocol
  Evaluate which events are generated when loads and stores operate with a simple directory cache coherence protocol

## Slide 4: Recall: Cache Coherence Problem
  Processors see different values for u after event 3
  With write back caches, value written back to memory depends on order of which cache writes back value first
  Unacceptable situation for programmers
I/O devices
Memory
P
1
$
$
$
P
2
P
3
5
u
= ?
4
u
= ?
u
:5
1
u
:5
2
u
:5
3
u
= 7

## Slide 5: Coherence Invariants
Single-Writer, Multiple-Reader (SWMR) Invariant
Data-Value Invariant. The value of the memory location at the start of an epoch is the same as the value of the memory location at the end of its last read-write epoch.
read-write
Core 0
read-only
Core 0,2
C0: store A
C2: load A
C3: store A
read-write
Core 3
read-only
Core 0,3
read-only
Core 0,1,3
C0: load A
C1: load A
Notes: Definition from: “A Primer on Memory Consistency and Cache Coherence” (an excellent book on the subject if you want to learn more).

## Slide 6: Coherence States
How to design system satisfying invariants?
Track “state” of memory block copies and ensure states changes satisfy invariants.
Typical states: “modified”, “shared”, “invalid”.
Mechanism for updating block state called a coherence protocol.

## Slide 7
Cache can be accessed by CPU () or Bus ().
We will consider effect of each starting with CPU.
Mem
P
1
$
$
P
n
Bus



## Slide 8: Implementing Cache Coherence
Core
Cache Controller
Cache
Interconnection Network
Requests received from both core and network:
Processor request:
  receive load/store from core
  update state of block
  issue coherence request
  receive response
  update state of block
  reply to core
Network request:
  receive coherence request
  update state of block
  issue coherence response
loads &
stores
loaded
values
issued
coherence
requests &
responses
received
coherence
requests &
responses

## Slide 9: Coherence, Simplified
Initially, assume all actions triggered by a memory request take place atomically. Only consider “stable” coherence states.
This view ignores time for messages to be sent and received.
In practice add “transient” states to enable multiple memory requests to occur in parallel.

## Slide 10: Coherence Protocol States
Logically, each memory block has a state.
Typically 2 to 5 states for each block.
Valid Dirty Tag Data
Direct mapped, write-back, write allocate
1
1
I
S
M
Valid | Dirty | State
0 | X | Invalid
1 | 0 | Shared
1 | 1 | Modified

## Slide 11: Directory vs. Snoop Protocols
Directory Coherence Protocol
  Summarize state of block in all caches in single location called a directory.
  Advantages: Scalability
  Disadvantage: Latency, Complexity
Snoop Coherence
  For each action ask all caches for state of block
  Advantages: Fast and simple
  Disadvantage: Not scalable
Stable states at L1 cache same for both

## Slide 12: Snooping Cache-Coherence Protocols
Cache Controller “snoops” all transactions on the shared medium (bus or switch)
  Relevant transaction if for a block it contains
  Take action to ensure coherence
    invalidate or supply value
  Action depends on state of the block and the protocol
Get exclusive access before write via write invalidate
State
Tag
Data

## Slide 13: MSI Snoop Protocol
Each memory block is in one state (state is implicit)
  Clean in all caches and up-to-date in memory (Shared)
  OR Dirty in exactly one cache (Modified)
  OR Not in any caches
Each cache block is in one state (state is explicit):
  Shared : block can be read
  OR Modified: cache has only copy, its writeable, and dirty
  OR Invalid : block contains stale data or never accessed
Read misses: cause all caches to snoop bus in case they have a modified copy of data (memory may be out of date)
Write hits to “shared” blocks: treated as misses since we need to tell other processor caches about the write so they can invalidate any shared copy of the data.

## Slide 14
Writes need to know whether any other copies of the block is cached
Write hit:
  Block in modified state  No other copies  No need to place invalidate on bus for writeback cache
  Block in shared state  may be copies  Need to place invalidate on bus (will cause other processors to invalidate their copy)
  Write miss:
  Block in invalid state  write miss  Need to read block from memory (as in uniprocessor case) or another processor (if modified state in that other processor’s cache).

## Slide 15: Write-Back State Machine – CPU
CPU Read hit
State machine for CPU requests for each cache block
Non-resident blocks invalid
Invalid
Shared
Modified
CPU Write
Place read miss
on bus
Place Write Miss on bus
CPU read hit
CPU write hit
Cache Block
State
CPU Read
CPU Write
Place Write Miss on Bus
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 16: Block-replacement
State machine for CPU requests for each cache block
Invalid
Shared
(read/only)
Modified
(read/write)
CPU read miss
Write back block,
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
Cache Block
State
CPU Read miss
Place read miss
on bus
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 17: Write-Back State Machine- Bus request
State machine for bus requests for each cache block
Invalid
Shared
(read/only)
Modified
(read/write)
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write miss for this block
Write Back
Block; (abort
memory access)
State Tag Data
I/O devices
Mem
P
1
$
$
P
n
Bus
State Tag Data

## Slide 18: Write-back State Machine-III
Place read miss
on bus
State machine for CPU requests for each cache block and for bus requests for each cache block
Invalid
Shared
(read/only)
Modified
(read/write)
CPU Read
CPU Write
CPU Read hit
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Write miss for this block
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write Back
Block; (abort
memory access)
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 19: Example
Bus-based shared-memory system.
Writeback invalidate snoop protocol.
Direct-mapped caches: 4 blocks, each with 2 words (word = 4B). two words separated by dotted line (smaller addresses on the right).
Tag contains the full address (in hex).
 | State | Tag | Data | 
B0 | I | 100 | 00 | 00
B1 | I | 108 | 00 | 00
B2 | S | 110 | 00 | 01
B3 | M | 118 | 80 | 40
P1
 | State | Tag | Data | 
B0 | M | 120 | 01 | 31
B1 | M | 128 | 54 | 40
B2 | S | 110 | 00 | 01
B3 | I | 118 | 80 | 00
P2
 | State | Tag | Data | 
B0 | I | 100 | 00 | 00
B1 | S | 108 | 42 | 00
B2 | I | 110 | DF | FF
B3 | M | 138 | 00 | 28
P3
 | State | Tag | Data | 
B0 | I | 100 | 00 | 00
B1 | S | 108 | 42 | 00
B2 | M | 130 | 00 | 02
B3 | I | 118 | 00 | 00
P4
100 | 
108 | 
110 | 
118 | 
120 | 
128 | 
130 | 
138 | 
140 | 
00 | 07
42 | 00
00 | 01
80 | 00
00 | 31
54 | 00
00 | 01
00 | 00
00 | 00
Memory
Address Data