## Slide 1: CPEN 411: Computer Architecture Slide Set #19: Cache Coherence, Part 2 Instructor: Dr. Tor M. Aamodt aamodt@ece.ubc.ca

## Slide 2: Learning Objectives
By the time we finish talking about this slide set in lectures you should be able to:
  Define true and false sharing, and coherency misses
  List three approaches to reduce false sharing
  Describe how a directory based cache coherence protocol differs from a snooping cache coherence protocol
  Evaluate which events are generated when loads and stores operate with a simple directory cache coherence protocol
  List/define several synchronization primitives
  Explain sequential consistency.

## Slide 3: Coherence Misses
Recall: Uniprocessor cache miss traffic
  3 C’s: Compulsory, Capacity, Conflict
New: Cache misses caused by communication
  Writing block in remote cache causes invalidation
  4th C: Coherence miss

## Slide 4: Coherence Misses
True sharing misses arise from the communication of data through the cache coherence mechanism
  First write to shared block
  Read miss of word modified by remote processor
  Note: Miss would still occur if block size were 1 word
False sharing misses arise when a block was invalidated because some word in the block was written to other than the one now being read or written
  Invalidation does not cause a new value to be communicated, but only causes an extra cache miss
  Block is shared, but no word in block is actually shared
  Note: Miss would not occur if block size were 1 word

## Slide 5: Example: True v. False Sharing v. Hit?
Time | P1 | P2 | True, False, Hit? Why?
1 | Write x1 |  | 
2 |  | Read x2 | 
3 | Write x1 |  | 
4 |  | Write x2 | 
5 | Read x2 |  | 
Assume x1 and x2 in same cache block. P1 and P2 both read x1 and x2 before.
True miss; invalidate x1 in P2
False miss; x2 irrelevant to P1
False miss; x1 irrelevant to P2
False miss; x2 irrelevant to P1
True miss; x2 wr in P2, rd in P1
1
0
Valid Dirty Tag Data
…x1 … x2 ...
Initial conditions (both caches):

## Slide 6: Impact on Coherence Misses: Cache Size
Uniprocessor cache misses improve with cache size increase (Instruction, Capacity/Conflict, Compulsory)
True sharing and false sharing unchanged going from 1 MB to 8 MB (L3 cache)
(Memory) Cycles per Instruction

## Slide 7: Impact on Coherence Misses: Processor Count
True sharing, false sharing increase going from 1 to 8 CPUs
(Memory) Cycles per Instruction

## Slide 8: Impact on Coherence Misses: Cache Size: Block Size
True sharing misses decrease due to locality in sharing patterns.
False sharing misses increase (more likely to have unrelated data stored on same cache block)

## Slide 9: Reducing False Sharing (1)
i
j
“float A[N][N]”
“float A[N/b][N/b][b][b]”
Consider how “float A[N][N];” is stored in memory: A[i][j+1] is adjacent to A[i][j] in memory, but A[i+1][j] is not adjacent to A[i][j].
Reduce false sharing by structure data to reduce “spatial interleaving” (e.g., using “higher order” arrays as illustrated in “b” above)

## Slide 10: Reducing False Sharing (2)
Beware using thread/process ID to index arrays:
  #define NCORES 4
  int g_foo[NCORES];
  ...
  g_foo[ tid ] ++; // BAD! FALSE SHARING!
Instead, “pad” to cache block size (so each processor accesses an element of g_foo on a different block)
  #define NCORES 4
  #define INTS_PER_BLOCK (32/sizeof(int)) /* for 32 B cache blocks */
  int g_foo[NCORES*INTS_PER_BLOCK];
  ...
  g_foo[ tid*INTS_PER_BLOCK ] ++; // GOOD! NO FALSE SHARING.

## Slide 11: Reducing False Sharing (3)
Consider carefully how to organize arrays of “structs” (or arrays of “objects”):
Consider “n-body problem” (physics).
Need to know position of all “particles”
to compute force on any given particle.
Parallelize so each processor computes
force on a particular particle.
Each processor wants to read position
of other particles to update force and
velocity of particle it is processing.
Position for each particle could be in
“shared state” in all processor caches,
but updates to force or velocity increase
false sharing misses in (a) versus (b).

## Slide 12: Directory Based Coherence
Problem: As number of processors increases, broadcast becomes too expensive.
Solution: Replace bus with scalable interconnection network (e.g., 2D mesh) and only send messages to caches containing blocks that need to change state.
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
CPU
$
P
1
$
Interconnection network
$
P
n
Mem
Mem
MEM
MEM
MEM
MEM
Multicore Processor with 2D mesh
Distributed shared memory multiprocessor
(interconnect might be 2D torus topology)

## Slide 13: Basic Operation of Directory
Each block in memory has a corresponding directory entry.
Directory entry contains “presence bits” and dirty bit.
If copy of block is in cache “i” then presence bit “i” is set to 1 (dot in figure).
Invalidate by sending messages to processors with presence bit set.




## Slide 14: Directory Protocol
Terminology: three processors involved
  Local node where a request originates
  Home node where the memory location of an address resides
  Remote node has a copy of a cache block, whether modified or shared
Example messages on next slide: P = processor number, A = address
P
L
$
Inter
connection network
$
P
R
Mem
Mem
P
H
$
Mem
LD R1,0(R2)
D
D
D

## Slide 15: Directory Protocol Messages
Message type Source Destination Msg Content
Read miss Local cache Home directory P, A
  Processor P reads data at address A; make P a read sharer and request data
Write miss Local cache Home directory P, A
  Processor P has a write miss at address A; make P the exclusive owner and request data
Invalidate Home directory Remote caches A
  Invalidate a shared copy at address A
Fetch Home directory Remote cache A
  Fetch the block at address A and send it to its home directory; change the state of A in the remote cache to shared
Fetch/Invalidate Home directory Remote cache A
  Fetch the block at address A and send it to its home directory; invalidate the block in the cache
Data value reply Home directory Local cache A, Data
  Return a data value from the home memory (read miss response)
Data write back Remote cache Home directory A, Data
  Write back a data value for address A
Other messages that might be used in a real implementation: Acknowledgements (ACK’s)

## Slide 16: CPU -Cache State Machine
State machine for CPU requests (+ requests from
home node) for
each memory block
Invalid state if in memory
Fetch/Invalidate
Invalidate
Invalid
Modified
(&Exclusive)
(read/write)
CPU Read
CPU Read hit
Send Read Miss
message
CPU Write:
CPU Write:
CPU read hit
CPU write hit
Fetch:
CPU read miss:
CPU write miss:
CPU read miss:
Shared
(read/only)
Send Read Miss
Send Write Miss
msg to home directory
CPU Write: Send Write Miss message
to home directory
Fetch:
CPU read miss: send Data Write Back message and read miss to home directory
CPU write miss:
send Data Write Back message
and Write Miss to home directory
Fetch/Invalidate
send Data Write Back message
to home directory
send Data Write Back message to home directory
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 17: Directory State Machine
State machine for Directory requests for each memory block
Uncached state if in memory
Data Write Back:
Sharers = {}
(Write back block)
Uncached
Shared
(read only)
Read miss:
Sharers = {P}
send Data Value
Reply
Write Miss:
send Invalidate
to Sharers;
then Sharers = {P};
send Data Value
Reply msg
Write Miss:
Sharers = {P};
send Data
Value Reply
msg
Read miss:
Sharers += {P};
send Fetch;
send Data Value Reply
msg to remote cache
(Write back block)
Read miss:
Sharers += {P};
send Data Value Reply
Write Miss:
Sharers = {P};
send Fetch/Invalidate;
send Data Value Reply
msg to remote cache
Modified
(&Exclusive)
(read/write)
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 18: Example Question
I | 100 | 00 | 80
S | 108 | 10 | 20
M | 110 | 00 | 01
S | 118 | 80 | 40
state tag data
I | 100 | 02 | 34
S | 108 | 10 | 20
I | 110 | 00 | 80
I | 118 | 00 | 42
I | 100 | 02 | 34
S | 108 | 10 | 20
I | 110 | 00 | 00
S | 118 | 80 | 40
I | 100 | 00 | 00
I | 108 | 00 | 42
M | 130 | 00 | 02
I | 118 | 00 | 00
state tag data
state tag data
state tag data
B0
B1
B2
B3
B0
B1
B2
B3
B0
B1
B2
B3
B0
B1
B2
B3
P0
P1
P2
P3
100 | DI |  | 00 | 00
108 | DS | P0,P1,P2 | 10 | 20
110 | DM | P0 | 00 | 80
118 | DS | P0,P2 | 80 | 40
120 | DI |  | 02 | 01
Writeback invalidate directory protocol.
Direct-mapped caches: 4 blocks, each with 2 words (word = 4B). two words separated by dotted line (smaller addresses on the right).
Tag contains the full address (in hex).

## Slide 19: Synchronization
Acquire method
  Acquire right to enter critical section, go past event
Waiting algorithm
  Wait for synch to become available when it isn’t
  busy-waiting, blocking, or hybrid
Release method
  Enable other processors to acquire right to the synch
Waiting algorithm is independent of type of synchronization
  makes no sense to put in hardware

## Slide 20: Strawman Lock
lock: LD R1,location /* copy location to register */
BNEZ R1,lock /* compare with 0, if not 0, try again */
SD location, #1 /* store 1 to mark it locked */
RET /* return control to caller */
unlock: SD location, #0 /* write 0 to location */
RET /* return control to caller */
Busy-Wait
Why doesn’t the acquire method (“lock”) work?
Release method OK?

## Slide 21: Atomic Instructions
Specifies a memory location, register, and an atomic operation
  Value in location read into a register
  Another value (maybe function of value read) stored into location
Many variants
  Varying degrees of flexibility in what is stored into location

## Slide 22: Simple Test & Set Lock
lock: t&s register, location
bnez register, lock /* if not 0, try again */
ret /* return control to caller */
unlock: sw location, #0 /* write 0 to location */
ret /* return control to caller */
Test&set (t&s) instruction:
  Value in location read into a specified register
  Constant 1 stored into location
  Successful if value loaded into register is 0
  Other constants could be used instead of 1 and 0

## Slide 23: Other Atomic Instructions
Atomic exchange: interchange a value in a register for a value in memory
  0  synchronization variable is free
  1  synchronization variable is locked and unavailable
  Use to implement test-and-set: Set register to 1 and then do atomic exchange. New value in register determines success in getting lock 0 if you succeeded in setting the lock (you were first) 1 if other processor had already claimed access
Fetch-and-increment: returns the value of a memory location and atomically increments it
  0  synchronization variable is free

## Slide 24: Load Locked, Store Conditional
Implementing atomic read-modify-write requires significant hardware changes and can cause poor performance for unrelated memory accesses.
An alternative to forcing the read-modify-write to be atomic is to instead detect when a read-modify-write did not execute atomically (some other operation accessed the value between the read and write).
“Load locked” also sometimes called “load linked”.

## Slide 25: Load Locked, Store Conditional
Load locked + store conditional
  Load locked returns initial value of memory location.
  Store conditional returns “1” if no other store wrote to same memory location since preceding load locked, and returns 0 otherwise.
  A return value of 0 means the sequence of load-locked and store conditional did not execute atomically. In this case, we might repeat the load locked and store conditional to try again.
  Load locked and store conditional can be used to implement a wide variety of atomic operations

## Slide 26: Examples
Atomic swap of “Regs[R4]” and “Mem[Regs[R1]]”
try: mov R3,R4 ; copy R4 ll R2,0(R1) ; load locked sc R3,0(R1) ; store conditional beqz R3,try ; branch if store conditional fails (R3 = 0) mov R4,R2 ; put load value in R4
Fetch & increment of “Mem[Regs[R1]]”
try: ll R2,0(R1) ; load locked addi R2,R2,#1 ; increment (OK if reg–reg) sc R2,0(R1) ; store conditional beqz R2,try ; branch store fails (R2 = 0)

## Slide 27: Spin Lock Performance
Spin locks: processor continuously tries to acquire, spinning around a loop trying to get the lock
ld R2,#1 lockit: exch R2,0(R1) ;atomic exchange bnez R2,lockit ;already locked?
What about cache coherency?
Problem: exchange includes a write, which invalidates all other copies; this generates considerable bus traffic.

## Slide 28: Test and test and set
For parallel programs with long critical sections, we can reduce bus traffic by first reading the variable using a normal load instruction which will cause a shared copy of the lock variable to be placed in the cache attached to the processor.
When a different processor modifies the location (to release the lock), the local version gets invalidated, then reloaded the next time the normal load instruction reads it. The new value of the memory location might indicate the lock is available and only then will we attempt to atomically perform a read-modify-write using a test and set instruction.
This is known as a “test and test&set” lock.
Example “test and test&set” using an atomic exchange instruction:
try: addui R2,R0,#1 lockit: ld R3,0(R1) ;normal load of Mem[Regs[R1]] bnez R3,lockit ; ≠ 0  not free  spin exch R2,0(R1) ;atomic exchange bnez R2,try ;already locked?